## Slide 1: ECE 382 Lesson 10
Lesson Outline
  The Stack
  Subroutines
  Lab 2 Intro
Admin
  MiniQuiz!! Next time
  Demo Lab 1 functionality by COB today!
  Assignment 4 due BOC next Lesson
  Lab 2 prelab due BOC next lesson

## Slide 2: Stack
What is a Stack?

## Slide 3: Stack
What is a Stack?
  Last In First Out (LIFO) queue
  Push and Pop are our two operations for dealing with the stack
  The last item you pushed onto the stack is the first item you'll pop off of it.
Why use a Stack?
  Temporary Storage
  Subroutine calls/returns use the Stack
Stack Pointer
  Holds the address of the top of the stack
    Stack Pointer (SP), also known as r1

## Slide 4: Stack
Stack Instructions
Where is the Stack located in memory?
Assembly Instruction | Description
PUSH(.B) | Push operand on stack. Push byte decrements SP by 2.
Emulated Instruction | Assembly Instruction
POP dst | MOV @SP+, dst

## Slide 5: Stack
Where is the Stack located in memory?
In RAM
- need to read and write to it
RAM is from 0x200 to 0x400
Where in RAM should you initialize the
Stack Point too?

## Slide 6: Stack
Where in RAM should you initialize the
Stack Point too?
0x400
0x200 would be bad!

## Slide 7: Stack
mov.w #0x0400, r1 ;initialize stack pointer
push.w #0xdfec ;push the value 0xdfec onto the stack.
;This decrements the SP by two to 0x03fe and
; stores EC at 0x03fe and DF at 0x03ff
pop.w r10 ;pop the value we just pushed off of the stack and
; into r10
; this decrements the SP by two, back to 0x0400.
push #0xbeef
push.b #0xcc
push #0xdfec
pop r5
pop.b r6
pop r7
push #0xfade
push.b #0xaa
push #0xdeaf
pop.b r5
pop r6
pop.b r7
Address | Value
0x3FA | 
0x3FB | 
0x3FC | 
0x3FD | 
0x3FE | 
0x3FF | 
0x400 | 

## Slide 8: Stack
How can I use the Stack to swap the values in two registers (like r10, r11)?
What happens if we do not initialize the stack pointer at the beginning of the program?
Can we push too many variables on the stack?
Is the stack limited?

## Slide 9: Subroutines
Why Subroutines?
  Supports Modularity; easier to read code; Supports re-use
  Call #SQ_ROOT
  …
  Call #SQ_ROOT
  …
  …
  SQ_ROOT: …
  …
  …
  RET
What happens in you didn’t initialize the Stack Pointer?
What If Stack Pointer pointed to ROM?
Assembly Instruction | Description
CALL | Fetch operand, push PC, then assign operand value to PC.
Emulated Instruction | Assembly Instruction
RET | MOV @SP+, PC
0xC010
0xC020

## Slide 10: Example Subroutine
main:
mov.w #2, r10
mov.w #4, r11
call #addition
nop
nop
nop
nop
addition:
add.w r10, r11
ret

## Slide 11: Arguments
Arguments are the parameters (or data) passed to and from a subroutine
  ;---------------------------------------------------
  ;Subroutine Name: Addition
  ;Author: Capt Jeff Falkinburg, USAF
  ;Function: Adds two numbers
  ;Inputs: operand1 in r10, operand2 in r11
  ;Outputs: result in r11
  ;Registers destroyed: r11
  ;---------------------------------------------------
  addition:
  add.w r10, r11
  ret
How could I avoid destroying registers used in a subroutine?

## Slide 12: Arguments
Use a stack to avoid destroying registers
  mySubroutine:
  push.w r5
  push.w r6
  push.w r7
  ;... Do subroutine work here ....
  pop.w r7
  pop.w r6
  pop.w r5
  ret
What is Pass-by-Value and Pass-by-Reference?

## Slide 13: Arguments
Pass-by-Value
  pass the actual values of the arguments to a subroutine
Pass-by-Reference
  Pass the address of the argument to a subroutine
Which did we do in the Addition subroutine?
Which method can modify the original source data, and which can only modify a copy of the source data?
Which is best if you are passing an array of 1000 values?

## Slide 14: Example Subroutine with pass-by-reference
;---------------------------------------------------
;Subroutine Name: Addition
;Author: Capt Jeff Falkinburg, USAF
;Function: Adds two numbers, returns the result
;Inputs: address of operand1 in r10, address of operand2 in r11
;Outputs: result in r11
;Registers destroyed: r11
;---------------------------------------------------
addition:
push.w r12
mov.w @r11, r12
add.w @r10, r12
mov.w r12, r11
pop r12

## Slide 15: Key Subroutine Rules
Always return from a subroutine!
  should only return from one place in your subroutine.
Subroutines only receive information via registers!
  reusable for many different programs
  should not rely on specific label names for arguments (what about ports?)
  Can we use the Stack to pass arguments?
Subroutines should be reusable!

## Slide 16: Application Binary Interface (ABI)
Convention of specifying which registers are used for arguments passed in to a subroutine and which are used to pass back results.
For subroutines in the MSP430 use r12, r13, r14, and r15 to pass arguments to your subroutine.
Use the stack if you have more than four arguments

## Slide 17: Lab 2 Introduction
The goal of this lab is to subroutines to decrypt some encrypted messages with keys of different lengths.
Lab 2