## Slide 1: ECE 382 Lesson 2
Readings
  Assembler Linker
Lesson Outline
  Intro to the MSP430
  MSP430 Architecture
  Assembly and Machine Languages
Admin
  Skills Review due next time!

## Slide 2: Intro to the MSP430
The MSP430 is an industry leader in low-cost, low-power consumption embedded applications
  RISC architecture with just 27 instructions.
  Products in the Wild Using MSP430
  Only $5
  Our version: MSP430G2553
What is an ISA?

## Slide 3: Instruction Set Architecture
Consists of
  set of operations (instructions)
  registers
  data units (byte/word/etc)
  addressing modes
  memory organization / memory map

## Slide 4: MSP430’s ISA
RISC architecture
  fewer instructions (27)
  emulates higher-level instructions (24)
    for instance, NOP  ___________
  16-bit datapath
    What is a datapath?

## Slide 5: MSP430’s ISA
  16-bit datapath
    word size is 16 bits
    word is the natural unit of info for the processor
      16 bit addresses
      16 bit registers
      all instructions are 16 bits long
      this consistency isn't necessarily true of all processors, but it's convenient - allows us to load addresses into registers, perform ops on them, etc.
What is a register?

## Slide 6: MSP430’s ISA
Registers - 16 bits wide
  Fast memory that holds values in-use by the CPU
  Four special purpose registers
    r0 - Program Counter - holds address of instruction currently being executed
    r1 - Stack Pointer - address of top of stack
    r2 - Status Register - holds flags related to various conditions
    r3 - Constant Generator - 0, but can assume other values for different addressing modes (L4)
  12 general purpose registers
    r4 to r15: can be used to hold anything you want

## Slide 7: MSP430’s ISA
Set of Operations
  27 Instructions in 3 families - we'll talk about these next time
    Two-operand
      for instance, MOV r12, r10
    Single-operand
      for instance, SWPB r12
    Jump
      for instance, JMP jump_label

## Slide 8: MSP430’s ISA
Data Units
  byte-addressable memory
  instructions for byte and word actions
    MOV.B r12, r10
    MOV.W r12, r10
  remember, word size is 16 bits
    words must lie on even addresses

## Slide 9: MSP430’s ISA
MSP430G2553 Memory Map
512B of RAM - 0x200-0x400 16kB of ROM - 0xc000-0xffdf
0x1100-0xbfff is empty!
- There is no memory backing it up!
- If you attempt to write to this area of memory, you'll trigger what's essentially a segmentation fault because that memory doesn't exist. It will cause the chip to do a Power-up Clear (PUC), resetting the state of your processor. This is a tough error to debug.
How many addr bits?
 |  | MSP430G2553
Memory Main: interrupt vector Main: code memory | Size Flash Flash | 16kB 0xFFFF to 0xFFC0 0xFFFF to 0xC000
Information memory | Size Flash | 256 Byte 010FFh to 01000h
RAM | Size | 512 Byte 0x03FF to 0x0200
Peripherals | 16-bit 8-bit 8-bit SFR | 01FFh to 0100h 0FFh to 010h 0Fh to 00h
Excerpt from Table 8: Memory Organization from MSP430G2x53 Device Specific User Guide (pp13) |  | 

## Slide 10: Big/Little Endian Byte Storage
There are two storage conventions: big endian and little endian
The value ABCD1234H would be stored as shown below for the different storage conventions
The name big/little endian answers the question: “What is stored in Byte #0?”
Byte zero holds Big Endian of the word
Byte zero holds Little Endian of the word
0
1
0
0
0
0
1
0
Byte #1
0
0
1
1
0
0
0
1
Low Order Byte
(Byte #0)
1
1
0
1
1
1
0
0
Byte #2
1
0
1
1
1
1
0
1
Byte #1
1
0
1
0
1
1
0
0
Low Order Byte
(Byte #0)
0
0
1
0
0
1
0
0
High Order Byte
(Byte #3)
0
0
0
1
0
0
1
1
Byte #2
(12)
(34)
1
0
1
1
High Order Byte
(Byte #3)
1
0
1
0
(AB)
(CD)
(CD)
(AB)
(34)
(12)

## Slide 11: MSP430Architecture Uses Little Endian
Values stored in little-endian byte order
Least significant byte is stored first
5000
5001
5002
5003

## Slide 12: MSP430’s ISA
Endianness
  concerned with the ordering of bytes on a computer.
  Little Endian means the least significant byte of a chunk of data is stored at the lowest memory address.
    MSP430 and your x86_64 are little endian
  Big Endian means the most significant byte of a chunk of data is stored at the lowest memory address.
    The 68S12 used in previous classes used this
If we executed MOV.W #0xdfec, &0x0200, how would that word be stored in memory?
addr | value
200 | 
201 | 
202 | 
203 | 
Debugger: 200

## Slide 13: Assembly and Machine Languages
Instructions:
  words in a computers language
Instruction Set:
  the dictionary of the language
Assembly Language:
  human-readable format of computer instructions
Machine Language:
  computer-readable instructions - binary (1's and 0's)
Assembler
Assembly Language Program
Linker
Relocatable Object Code
Executable Code

## Slide 14: Steps for Translating and starting a program
Compiler
Assembler
Higher Level Language (HLL)
Assembly Language
Object File (Machine Code)
Linker
Executable
Loader
Memory
Object Files
Library Files

## Slide 15: Let's write our first MSP430 program
; This program sets all pins on Port 1 to output and high. Since LEDs 1 and 2 are connected to P1.0 and P1.6 respectively, they will light up.
.include 'header.S'
.text
main:
mov.w #WDTPW, r15 ; turn off watchdog timer
xor.w #WDTHOLD, r15
mov.w r15, &WDTCTL
bis.b #0xFF, &P1DIR ; set port1 direction to output
bis.b #0xFF, &P1OUT ; turn on leds at port1
loop:
jmp loop ; loop forever

## Slide 16: Example Relocatable Code
Notice the addresses - the code starts at 0x0.
Hex dump of section '.text':
0x00000000 3f40005a 3fe08000 824f2001 f2d32200
0x00000010 f2d32100 b0120000 ff3f
After Linking
Notice the addresses - the code starts at 0xC000.
Hex dump of section '.text':
0x0000c000 3f40005a 3fe08000 824f2001 f2d32200
0x0000c010 f2d32100 b0121ac0 ff3fc243 21003041

## Slide 17: Example Dissassembled Code
Disassembly of section .text:
0000c000 <__ctors_end>:
c000: 3f 40 00 5a mov #23040, r15 ;#0x5a00
c004: 3f e0 80 00 xor #128, r15 ;#0x0080
c008: 82 4f 20 01 mov r15, &0x0120
c00c: f2 d3 22 00 bis.b #-1, &0x0022 ;r3 As==11
c010: f2 d3 21 00 bis.b #-1, &0x0021 ;r3 As==11
0000c014 <loop>:
c014: ff 3f jmp $+0 ;abs 0xc014

## Slide 18
Code Composer Studio demo…