## Slide 1: ECE 382 Lesson 19
Lesson Outline
  High-Level Programming Languages
  Compilers
  Intro to C
Admin
  GR#1
    Know for FINAL EXAM!
  Lab 3 due midnight Sunday (not 0001 Monday morning)
  Assignment 6 due BOC next Lesson

## Slide 2: High Level Language versus Assembly
I'm a Compiler
List of Programming Languages
Benefits of using these over programming in assembly?

## Slide 3: High Level Language versus Assembly
I'm a Compiler
List of Programming Languages
Benefits of using these over programming in assembly?
  Ease of development
    HLLs offer constructs that allow us to develop code faster
      Loops
      conditional statements (if/then)
      Functions
      memory management (for some)
  Portability
    HLL code can be made to run on many different machines, whereas assembly is architecture-specific
  Readability
    HLL code is generally easier to read / understand than assembly
  Optimization
    Humans typically aren't that great at writing assembly code
    HLLs can offer optimization techniques / restrictions that can improve poorly-written code

## Slide 4: High Level Language versus Assembly
Some perspective: everything that happens on a computer is machine code. What do we use to generate machine code? The assembler. So every program you write ultimately becomes assembly code, then machine code

## Slide 5: Compiler
Assembler
Assembly Code
Linker
Relocatable Object Code
Executable Code
Compiler
High Level Language Program

## Slide 6: Compiler
Assembler
Assembly Code
Linker
Relocatable Object Code
Executable Code
Compiler
High Level Language Program
Cross-Assembler
Assembly Code
Linker
Relocatable Object Code
Executable Code
Cross-Compiler
High Level Language Program

## Slide 7: Compiler
Compiled Language versus Interpreted?
Examples:
Any Advantages of Assembly over HLL?

## Slide 8: Compiler
Compiled Language versus Interpreted?
Examples:
Fast  Portable
Any Advantages of Assembly over HLL?
Compiled | Both | Interpreted
C | Java | Python
C++ | C# | Prolog
Ada |  | Matlab
 |  | Scheme
 |  | Ruby

## Slide 9: Compiler
Compiled Language versus Interpreted?
Examples:
Fast  Portable
Any Advantages of Assembly over HLL?
  HLL do not use all features of a chip
  HLL has less control over generated code
  HLL runs slower (usually)
Compiled | Both | Interpreted
C | Java | Python
C++ | C# | Prolog
Ada |  | Matlab
 |  | Scheme
 |  | Ruby

## Slide 10: Why C?
One of the most widely used programming languages of all time
Examples of projects coded in C:
  Kernel / OS: Linux, GNU
  Version Control: git
  Web Server: Apache, nginx
  Interpreter: Ruby, Python
  Databases: mysql, postgresql, redis
  Virtualization: vmware
  Almost anything embedded, device drivers
C is like a portable, higher-level assembly

## Slide 11: C Language: Comments
// Single line comment
/* block comment that can span
multiple lines */
int i = 0; // a declaration
/*************************************
** The previous variable was
** declared just as an example.
*************************************/

## Slide 12: C Language: Variables
•Note: These sizes are dependent on the compiler and target architecture - these are for the MSP430.
•Note: Do not use the float / double types on the MSP430 - since it doesn't have floating point hardware support, implementing software support will use almost all of your memory.
Type | Size | Description
char | 1 byte | number or ASCII character
int | 2 bytes | larger number
float | 2 bytes | single-precision floating point number
double | 4 bytes | double-precision floating point number
Variable Types

## Slide 13: C Language: Variables
•Note: Once again, sizes are dependent on compiler / target architecture - these are for the MSP
Variable Modifiers
Modifier | Description
short | remains a 2-byte integer
long | increases int size to 4 bytes
signed | two's complement numbers (default)
unsigned | allows unsigned arithmetic
static | directly allocates memory to remember a value between function calls. Variable is allocated to "permanent" memory, not the stack.
extern | actual storage and initial value of variable is defined elsewhere
const | assigns a constant (read-only) value to a variable

## Slide 14: C Language: Constants
Preferred Constant Declaration
The #define statement is a pre-processor directive.
pre-processor will “find-replace” each instant
similar to a .equ statement in assembly.
// #define MY_CONST some_value
#define SCREEN_WIDTH 640
#define SCREEN_HEIGHT 480
int numPixels = 0;
numPixels = SCREEN_WIDTH * SCREEN_HEIGHT;
•Note: There is no ';' or '=' in #define statements
•Note: Variables must be declared at the top of a block, and they are not initialized by default. A block is denoted by braces {}
•Note: A value can be binary (0b), octal (0), or hex (0x) by using prefixes

## Slide 15: C Language: Operators
Assignment, Arithmetic Operators
char myVar, a, b; // variable declaration
myVar = a; // assignment - note, all vars have undefined values at this point
myVar = a + b; // addition
myVar = a - b; // subtraction
myVar = a * b; // multiplication
myVar = a / b; // division
myVar = a % b; // modulus (remainder)
myVar++; // increment
myVar--; // decrement
myVar += a; // myVar = myVar + a
myVar -= a; // myVar = myVar - a

## Slide 16: C Language: Operators
Relational Operators
if ((a < 10) && (a > 5))
{
// literally: if a is greater than 5 and less than 10, do whatever is in here
// practically: if a is between 5 and 10, do whatever is in here
}
•Note: In C, "false" is 0, while any non-zero value is considered true.
Operator | Description | Example
< | less than | 
<= | less than or equal to | 
> | greater than | 
>= | greater than or equal to | 
== | equal to | 
!= | not equal to | 
&& | logical AND | 
¦ ¦ | logical OR | 

## Slide 17: C Language: Operators
Bit-wise Operators
// Example with SPI
UCA0CTL1 &= ~UCSWRST; // disable the subsystem (AND UCA0CTL1 with NOT UCSWRST)
UCA0CTL1 |= UCSWRST; // enable the subsystem (OR UCA0CTL1 with UCSWRST)
Operator | Description | Example
& | AND | 
¦ | OR | 
^ | XOR | 
~ | One's Complement | 
>> | Bit-shift right | 
<< | Bit-shift left | 

## Slide 18: If Statement
  if (logical expression)
  {
  statements;
  } else if (logical expression)
  {
  statements;
  }
  ...
  else
  {
  statements;
  }
Example:
  if (temp < MIN_TEMP)
  {
  flag = TOO_LOW;
  } else if (temp > MAX_TEMP)
  {
  flag = TOO_HIGH;
  }
  else
  {
  flag = JUST_RIGHT;
  }

## Slide 19: Switch Statement
  switch (value)
  {
  case constant-expression1:
  statements;
  break;
  case constant-expression2:
  statements;
  break;
  default:
  // gets executed if no other case hits
  statements;
  break;
  }
Example:
  switch (GAME_STATE)
  {
  case MENU:
  displayMenu();
  break;
  case PLAYING:
  updateState();
  break;
  case LOST:
  displayLost();
  break;
  }

## Slide 20: For Loop
  for (initial; continue; increment)
  {
  statements;
  }
initial - evaluated once, immediately before the first iteration of the loop. Usually used to initialize variable.
continue - condition checked to execute the next iteration. If false, then the loop terminates.
increment - single statement executed at the end of each loop. Usually used to increment / decrement a variable.
Example:
  for (i = 1; i <= 20; i++)
  {
  sum += i;
  }

## Slide 21: While / Do While Loop
  while (condition) {
  statements;
  }
  do while is guaranteed to be executed once, while isn't.
  do
  {
  statements;
  } while (condition);
Example:
  int i = 5;
  while (i < 10)
  {
  i++;
  }
  do {
  i++
  } while (i < 10);
  // final value of i is 11

## Slide 22: Basic C Program Structure
  // #include statements
  // #define statements
  // global variables
  void main(void)
  {
  // Variable declarations
  // Useful code
  while (1) {} // trap the CPU
  }
Example:
  #include <stdio.h>
  #include “math.h"
  #define NUM_LOOPS 23
  void main(void)
  {
  unsigned char i;
  unsigned int summation = 0;
  for (i = 1; i <= NUM_LOOPS; i++)
  {
  summation += i;
  }
  while (1) {} // trap the CPU
  }

## Slide 23: Headers !!!!
  /*******************************************
  * Author: George York
  * Created: 6 Oct 2014
  * Description: This is an example header!
  *******************************************/
  Try Assignment 5:
  http://ece382.com/notes/L20/L20_C_basics.html