## Slide 1: ECE 382 Lesson 32
Lesson Outline
  Lab 6 Introduction
  Pulse Width Modulation
  Capture / Compare
  Example
  Lab 6 Tips
Admin
  Lab#6 “prelab” due BOC lesson 33

## Slide 2: Lab#6: Robot Motion
Prelab:
  Software Design (flowchart and/or pseudo-code)
  Hardware Schematics
Basic Functionality:
  Move the Robot Forward, Reverse, Left, Right (small and large turn) (no USB cord)
A Functionality:
  Move the Robot Forward, Reverse, Left, Right using the IR remote control

## Slide 3: Using DC Motors
How do DC motors work? How do you make them go faster?

## Slide 4: Using DC Motors
How do DC motors work? How do you make them go faster?
  Provide analog DC voltage… The higher the voltage, the faster it spins
  [ motor demo ]

## Slide 5: Using DC Motors
How do DC motors work? How do you make them go faster?
  Provide analog DC voltage… The higher the voltage, the faster it spins
  [ motor demo ]
How to we control a DC motor with the MSP430 ?
Can we use the ADC converter?

## Slide 6: Using DC Motors
How do DC motors work? How do you make them go faster?
  Provide analog DC voltage… The higher the voltage, the faster it spins
  [ motor demo ]
How to we control a DC motor with the MSP430 ?
Can we use the ADC converter?
Two issues interfacing MSP430 with a DC motor?

## Slide 7: Using DC Motors
How do DC motors work? How do you make them go faster?
  Provide analog DC voltage… The higher the voltage, the faster it spins
  [ motor demo ]
How to we control a DC motor with the MSP430 ?
Can we use the ADC converter?
Two issues interfacing MSP430 with a DC motor?
  MSP430 only produces two voltages (Vcc and Gnd)
Solution?.

## Slide 8: Using DC Motors
How do DC motors work? How do you make them go faster?
  Provide analog DC voltage… The higher the voltage, the faster it spins
  [ motor demo ]
How to we control a DC motor with the MSP430 ?
Can we use the ADC converter?
Two issues interfacing MSP430 with a DC motor?
  MSP430 only produces two voltages (Vcc and Gnd)
Solution? PWM- pulse width modulation (remember this?)

## Slide 9: Using DC Motors
How do DC motors work? How do you make them go faster?
  Provide analog DC voltage… The higher the voltage, the faster it spins
  [ motor demo ]
How to we control a DC motor with the MSP430 ?
Can we use the ADC converter?
Two issues interfacing MSP430 with a DC motor?
  MSP430 only produces two voltages (Vcc and Gnd)
Solution? PWM- pulse width modulation (remember this?)
  MSP430 does not source enough current to power the motors (blow the chip)

## Slide 10: Using DC Motors
How do DC motors work? How do you make them go faster?
  Provide analog DC voltage… The higher the voltage, the faster it spins
  [ motor demo ]
How to we control a DC motor with the MSP430 ?
Can we use the ADC converter?
Two issues interfacing MSP430 with a DC motor?
  MSP430 only produces two voltages (Vcc and Gnd)
Solution? PWM- pulse width modulation (remember this?)
  MSP430 does not source enough current to power the motors (blow the chip)
Solution?

## Slide 11: Using DC Motors
How do DC motors work? How do you make them go faster?
  Provide analog DC voltage… The higher the voltage, the faster it spins
  [ motor demo ]
How to we control a DC motor with the MSP430 ?
Can we use the ADC converter?
Two issues interfacing MSP430 with a DC motor?
  MSP430 only produces two voltages (Vcc and Gnd)
Solution? PWM- pulse width modulation (remember this?)
  MSP430 does not source enough current to power the motors (blow the chip)
Solution? Motor driver chip (SN754410)
MSP430 Timer system helps
Input Capture: Monitor a pin for a specified signal (rising edge, falling edge, either edge) and record when it occurs.
Output Compare: Generate a specified signal with precise timing. (can make a PWM signal)

## Slide 12: Timer Block Diagram

## Slide 13: Backup Slides

## Slide 14: Input Capture
Capture mode is selected when the CAP bit in TACCTL is set to 1. It's used to record time events. It can be used for:
  Event detection
  Event counting
  Pulse-width measurement
  Frequency measurement
Each TACCRx has two possible capture pins - CCIxA and CCIxB. The one being monitored is selectable by software.
If a capture occurs: - The TAR value is copied into the TACCRx register - The interrupt flag CCIFG is set

## Slide 15: Input Capture

## Slide 16: Output Compare
Compare mode is selected when the CAP bit in TACCTL is set to 0
Same Timer Modes: MCx
Count up to TACCRO. Now adding two new registers: TA0CCR1 and TA0CCR2
Mcx | Mode | Description
00 | Stop | The timer is halted. MC_0
01 | Up | The timer repeatedly counts from zero to the value of TACCR0. MC_1
10 | Continuous | The timer repeatedly counts from zero to 0FFFFh. MC_2
11 | Up/down | The timer repeatedly counts from zero up to the value of TACCR0 and back down to zero. MC_3

## Slide 17: Output Compare

## Slide 18: Example
#include <msp430.h>
int main(void)
{
WDTCTL = WDTPW|WDTHOLD; // stop the watchdog timer
P1DIR |= BIT2; // TA0CCR1 on P1.2
P1SEL |= BIT2; // TA0CCR1 on P1.2
TA0CTL &= ~MC1|MC0; // stop timer A0
TA0CTL |= TACLR; // clear timer A0
TA0CTL |= TASSEL1; // configure for SMCLK
TA0CCR0 = 100; // set signal period to 100 clock cycles (~100 microseconds)
TA0CCR1 = 25; // set duty cycle to 25/100 (25%)
TA0CCTL1 |= OUTMOD_7; // set TACCTL1 to Reset / Set mode
TA0CTL |= MC0; // count up
while (1) {
__delay_cycles(1000000);
TA0CCR1 = 50; // set duty cycle to 50/100 (50%)
__delay_cycles(1000000);
TA0CCR1 = 75; // set duty cycle to 75/100 (75%)
__delay_cycles(1000000);
TA0CCR1 = 100; // set duty cycle to 100/100 (100%)
__delay_cycles(1000000);
TA0CCR1 = 25; // set duty cycle to 25/100 (25%)
}
return 0;
}

## Slide 19: Ports?
Pin 3 TA0.0 P1.1
Pin 4 TA0.1 P1.2
Pin 8 TA1.0 P2.0
Pin 9 TA1.1 P2.1

## Slide 20: Lab Tips
Drives like a tank? How do you turn?
Motor Driver Chip
You cannot hook your MSP430 directly up to the motors - it can't supply enough current! We need to use a motor driver chip instead. It can only supply 1A per circuit! Do not exceed that! Check out the datasheet for wiring details.
  http://ece382.com/datasheets/SN754410.pdf
Motor Stall Current
This is the max current draw your motor might have - usually happens when it runs up against the wall or something. This better not exceed the 1A your motor driver chip can supply or you'll burn it!
[Show technique to measure stall current]
On my robot, the stall current does not go below one amp until my motor is being driven at 8V or less - roughly 60% duty cycle. Exceed this at your own risk!

## Slide 21: Lab Tips
MSP430 In-Circuit
Supplying Power
  We have 3.3V regulators! Use them! If you try to give 5V to your MSP430, you will fry it! Check out the datasheet for wiring details.
  http://ece382.com/datasheets/LD1117V33.pdf
Wiring it up
  http://ece382.com/datasheets/robot.html
Programming
  See the tutorial on the website! You can just jump the VCC / TEST / RESET signal over to the chip on the breadboard.
  http://ece382.com/datasheets/in_circuit_programming.html
  http://ece382.com/datasheets/standalone.html
Chip Reset Due to Current Fluctuation
  If the motors draw a large amount of current (due to stall), there is a good chance it will interfere with the current provided to your MSP430. To combat this, you can put a large capacitor across the 5V rail (between power and ground). This will supplement the lost current and prevent your chip from being reset.

## Slide 22: Lab Details
http://ece.ninja/382/labs/lab6/index.html

## Slide 23
Backup slides

## Slide 24: Timer (p 355 User’s Guide)

## Slide 25: Multiplexing
Only 20 Pins !!! But want access to many more signals
  Therefore, each pin shares several signals  multiplexing
Use PxSEL1 and PxSEL2 to select signal for each pin
  The details are in the MSP430G2x53 2x13 Mixed Signal MCU Datasheet.

## Slide 26: Pitfall !!!

## Slide 28: Interrupt Vector Table