## Slide 1: ECE 382 Lesson 7
Lesson Outline
  Miniquiz
  Instruction Execution Time
  Watchdog Timer
  Clock
  Assembler Directives
  Structured Design and Test
  Lab Guidance
  Lab 1 Introduction
  Assignment 3
Admin
  Miniquiz next time
  Assignment 3 (due lesson 8)

## Slide 2: Instruction Execution Time
Clock is roughly 1 MHz
  What is the Clock Period?
So how long does this block of code take to execute?
  mov #0x0200, r5
  mov #0xbeef, 0(r5)
  forever jmp forever
Single Operand
  TI MSP 430 User’s Manual pp 60 (Blue Book pp18)
Two Operand
  TI MSP 430 User’s Manual pp 61 (Blue Book pp19)
Jumps
  All take 2 Cycles
  TI MSP 430 User’s Manual pp 60 (Blue Book pp18)

## Slide 3: Watchdog Timer
TI MSP 430 User’s Manual pp 341-347 (Blue Book pp 42-44)
If not disarmed, How long to reset?
  It counts 32768 clock cycles, then resets
15 | 14 | 13 | 12 | 11 | 10 | 9 | 8
WDTPW |  |  |  |  |  |  | 
7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
WDTHOLD | WDTNMIES | WDTNMI | WDTTMSEL | WDTCNTCL | WDTSSEL | WDTISx | 

## Slide 4: Watchdog Timer
;disable watchdog timer
mov #WDTPW, r10 ; to prevent inadvertent writing, the watchdog has a password - if you write without the password in the upper 8 bits, you'll initiate a PUC.
;the password is 0x5a in the upper 8 bits. if you read from the password, you'll read 0x69.
bis #WDTHOLD, r10 ; next, we need to bis the password with the bit that tells the timer to hold, not count
mov r10, &WDTCTL ; next, we need to write that value to the WDTCTL - this is a static address in memory (not relative to our code), so we need

## Slide 5: Assembler Directives
.cdecls C,LIST,"msp430.h"
.text ;put code in the text section - maps to FLASH (ROM)
StopWDT mov.w #WDTPW|WDTHOLD
.data ;put code into the data section - maps to RAM
.sect ".reset" ;put this at the reset vector
.sect .stack ;make this the location of the stack
MY_RESULTS: .space 20 ; reserves 20 bytes
-----------------
To use:
mov #MY_RESULTS, r5 ; pointer address into r5
mov #0xfefe, &MY_RESULT ; put fefe into 1st two bytes

## Slide 6: Assembler Directives
; Can initialize ROM; cannot initialize RAM
;initialize sequence of bytes
bytes: .byte 9,8,7,6,5,4,3,2,1
;initialize sequence of words
words: .word 0x1111,0x2222,0x3333,0x4444
;initialize strings
myStr: .string "hello, world!"
;initialize characters
Chars: .char 'a','b','c','d‘
; see in CCS

## Slide 7: Assembler Directives
; .equ  assign a label to a particular value
SEVENTEEN: .equ 0x11
;align a variable with a particular multiple of bytes (useful to ensure word on even address)
.align 2
;probably won't use these often, but they're available
.float ;floating point value
.int ;16-bit int
.short ;16-bit int
.long ;32-bit int

## Slide 8: Structured Design and Test
Guiding Principle: Get one small thing working
  Don't write the entire program in one go, then press go, and hope it works. When the entire program is the space you're looking for a bug, it makes debugging really hard.
Modularity
  Modularity is the practice of breaking down a larger program into smaller tasks.
  Makes code more reusable
  Makes code more readable
  Make individual taks more manageable
    Focus on simpler tasks
    Tough to hold a big problem in your brain

## Slide 9
Example Design
Concurrent Processes
Init
Got msg?
Yes
No
Init
Send Msg
Init
Send Ack
Init
Write
Image
Init
Do math
Got Ack?
No
Yes
Msg#1
Ack#1
Process image
New image?
Yes
No
Read Image
New = 1
Read data
FIFO
Write data
New data?
Yes
No
Done?
No
Yes
Do math
Done?
No
Yes
Do math
locked?
Lock
locked?
count++
Data#2
Data#2
Locked?
Locked?
Lock
Lock
Lock
No
No
Yes
Yes
Write Data
Write D
Read D
Read Data
Done?
Done?
No
Yes
Yes
No
Process#1
Process#2
Process#3
Process#4
Memory
Memory
New = 1
image
image
count
count--
New = 0
unlock
unlock

## Slide 10: Testing
How do we know when we're done with a task? Testing!
  You should specify the tests you'll run on the code you're going to write in advance of writing the code. It's a little more work up front, but will save you time debugging down the road.
Write tests that cover all cases - particularly edge cases.

## Slide 11: Lab Notebook Expectations
Lab Notebook Standards
Things people usually mess up:
  Not testing
  Testing after demonstration
  No hardware design
  Poorly written / commented code
  Post-filling notebooks (or Bitbucket readme.md)

## Slide 12: Assembly Code Style Guidelines
Comments
  Assume the reader is a competent assembly language programmer
  Comment above blocks of code to convey purpose
  Only comment individual lines when purpose is unclear
Labels
  Descriptive!
    loop or loop1 or l1 or blah - not acceptable!
Constants
  Use .equ syntax for all constants!
  Don't want to see naked values

## Slide 13: Assembly Code Style Guidelines
Instruction Choice
  Use the instruction that makes your code readable!
    JHS rather than JC
    INCD rather than ADD #2
  Well-written code requires few comments
Spacing
  Align your code to make it readable
  Put whitespace between logical blocks of code

## Slide 14: Programming Exercise
Write a program that will write your name in memory 6 times:
Can use:
myStr: .string “Jeff Falkinburg!"

## Slide 15: Example Code
What is good and bad about this code?
  http://ece.ninja/382/notes/L8/hw_sample.html

## Slide 16: Lab 1 Introduction
The goal of this lab is to implement a simple calculator using assembly language.
Lab 1
How This Lesson Applies
Use assembler directives:
  .byte to put your test program into memory
  .space to reserve space for your results
    Where is this going to go?
Labels for your program / results
.equ for key constants
Modularity
  Section to store results of ops
  Section for each op
Testing
  Specify multiple testing sequences at the beginning!
  I'll test your code with a few of my own

## Slide 17: Arithmetic Instructions
Add
Opcode | Assembly Instruction | Description | Notes
0101 | ADD src, dest | dest += src | 
0110 | ADDC src, dest | dest += src + C | 

## Slide 18: Arithmetic Instructions
mov #0xabab, r10
add #0xabab, r10 ; sets C and V
addc #2, r10

## Slide 19: Arithmetic Instructions
Subtract
For SUBC, think about it as flipping the carry bit! If C=1, it won't subtract the carry. If C=0, it will.
Opcode | Assembly Instruction | Description | Notes
0111 | SUBC src, dest | dest += ~src + C | 
1001 | SUB src, dest | dest -= src | Implemented as dest += ~src + 1

## Slide 20: Arithmetic Instructions
mov #5, r10
sub #8, r10 ; which flags will be set? carry because we're adding the 2's complement! Remember - 2's complement is 1 + bitwise not
subc #1, r10 ; expected result
mov #5, r10
sub #4, r10
subc #1, r10 ; weird result - what's going on here? Watch out for SUBC - can be confusing!

## Slide 21: Arithmetic Instructions
DADD
Show DADD in datasheet to illustrate use of carry bit.
Opcode | Assembly Instruction | Description | Notes
1001 | CMP src, dest | dest - src | Sets status only; the destination is not written.
1010 | DADD src, dest | dest += src + C, BCD (Binary Coded Decimal) | 

## Slide 22: Arithmetic Instructions
mov #5, r10
cmp #10, r10 ;evaluates 1-10, sets negative flag - remember, subtraction involves adding the 2's complement (a bit-wise invert + 1)
subc #1, r10 ; still weird!
mov #10, r10
cmp #1, r10 ;evaluates 10-1, sets carry flag - remember, subtraction involves adding the 2's complement (a bit-wise invert + 1)

## Slide 23: Arithmetic Instructions
DADD does binary coded decimal (BCD) addition.
In BCD, each nibble represents a binary digit.
So if I used DADD to add 0x0009 and 0x1, the result would be 0x0010 - not 0x000A.
This can actually be very useful if you're recording a value for later output in decimal.
Another note - DADD also adds the carry bit!
If you want a pure add, clear the carry first.

## Slide 24: Arithmetic Instructions
clrc
mov #0x99, r10
dadd #1, r10
setc
dadd #1, r10 ; DADD uses the carry bit!

## Slide 25: Emulated Arithmetic Instructions
The assembler provides some emulated increment / decrement commands. The D postfix means double - so it will increment or decrement by 2.
Emulated Instruction | Assembly Instruction
DEC(.B) dst | SUB(.B) #1, dst
DECD(.B) dst | SUB(.B) #2, dst
INC(.B) dst | ADD(.B) #1, dst
INCD(.B) dst | ADD(.B) #2, dst

## Slide 26: Emulated Arithmetic Instructions
SBC only works when the carry is clear!
This final set of emulated instructions allows you to add or subtract the carry bit by itself.
Emulated Instruction | Assembly Instruction
ADC(.B) dst | ADDC(.B) #0, dst
DADC(.B) dst | DADD(.B) #0, dst
SBC(.B) dst | SUBC(.B) #0, dst

## Slide 27: Emulated Arithmetic Instructions
incd r10
dec r10
sbc r10 ;why doesn't this subtract one? think about what the operation is doing
clrc
sbc r10
setc
adc r10

## Slide 28: Logic Instructions
These instructions can be very useful for manipulating / testing individual bits.
They're the foundation for the emulated instructions we talked about last time that set or clear flags in the Status Register.
Opcode | Assembly Instruction | Description | Notes
1011 | BIT src, dest | dest & src | Sets status only; the destination is not written.
1100 | BIC src, dest | dest &= ~src | The status flags are NOT set.
1101 | BIS src, dest | dest ¦=src | The status flags are NOT set.

## Slide 29: Logic Instructions
mov #1, r5
bit #1b, r5
bit #10b, r5
bit #100b, r5
mov.b #0xff, &P1OUT
mov.b #0xff, &P1DIR
bic #1b, &P1OUT
bic #1000000b, &P1OUT
bis #1b, &P1OUT
bis #1000000b, &P1OUT

## Slide 30: Logic Instructions
Logical operators AND and XOR are available as well.
These operations set status flags, while the BIC / BIS operators don't.
Opcode | Assembly Instruction | Description | Notes
1110 | XOR src, dest | dest ^= src | 
1111 | AND src, dest | dest &= src | 

## Slide 31: Logic Instructions
mov #0xdfec, r12
mov #0, r11
setc
and r11, r12
mov #0x5555, r11
xor #0xffff, r11

## Slide 32: Logic Instructions
There are a few emulated logical instructions: INV, CLR, and TST.
TST has unique behavior in that it always clears the V flag and set the C flag. N and Z are set as expected.
INV will flip all of the bits, CLR sets all bits to 0, TST compares the dst to 0.
Emulated Instruction | Assembly Instruction | Notes
INV(.B) dst | XOR(.B) #-1, dst | Sets overflow if result sign is different than inputs
CLR(.B) dst | MOV(.B) #0, dst | No flags set, since it's a MOV
TST(.B) dst | CMP(.B) #0, dst | V always clear, C always set

## Slide 33: Logic Instructions
mov #0xec00, r10
inv r10 ;$r10 is 0x13ff, set overflow and carry flags
bic #100000000b, r2 ;clear overflow bit
mov #0x8000, r10
inv r10 ;$r10 is 0x7fff, set overflow and carry flags
clr r10 ;$r10 is 0 - status flags not set because this is a mov instruction
tst r10 ;set zero, carry flags
inv r10 ;$r10 is 0xffff, set negative and carry flags
tst r10 ;set negative, carry flags

## Slide 34: Shift/Rotate Instructions
RRC is great for divide by 2 - if carry clear.
RRA is great for signed divide by 2.
Opcode | Assembly Instruction | Description
000 | RRC(.B) | 9-bit rotate right through carry. C->msbit->...->lsbit->C. Clear the carry bit beforehand to do a logical right shift.
001 | SWPB | Swap 8-bit register halves. No byte form.
010 | RRA(.B) | Badly named, this is an arithmetic right shift - meaning the most significant bit is preserved. LSB moves into carry.
011 | SXT | Sign extend 8 bits to 16. No byte form.

## Slide 35: Shift/Rotate Instructions
If the carry is cleared, RRC is a logical right shift. RRA is an arithmetic right shift. Since the MSB is preserved, this is a way to divide by 2. Since the LSB is discarded, the result is always rounded down.
SXT sign extends the MSB of the lower byte into the upper byte. SWPB sways 8-bit register halves.

## Slide 36: Shift/Rotate Instructions
clrc
mov #10010101b, r10
rrc.b r10 ;r10 is now 01001010, carry is set
rrc.b r10 ;r10 is now 10100101, carry bit is clear
rra.b r10 ;r10 is now 11010010, carry bit is set
rra.b r10 ;r10 is now 11101001, carry bit is clear
swpb r10
swpb r10
sxt r10

## Slide 37: Shift/Rotate Instructions
Rotate left is emulated by addition. A rotate left is the equivalent of multiplication by two, so it is emulated by adding the destination to itself.
RLA is not arithmetic - doesn't preserve most significant bit. Carry comes in on the right for RLC.
Emulated Instruction | Assembly Instruction
RLA(.B) | ADD(.B) dst, dst
RLC(.B) | ADDC(.B) dst, dst

## Slide 38: Shift/Rotate Instructions
mov #2, r10
rla r10 ;$r10 is now 0x4
rla r10 ;$r10 is now 0x8
setc
rlc r10 ;$r10 is now 0b10001, or 0x11

## Slide 39: MSP430’s ISA
Msp430g2553 Memory Map
512b of RAM - 0x200-0x400 16kb of ROM - 0xc000-0xffdf
0x1100-0xc000 is empty!
- There is no memory backing it up!
- If you attempt to write to this area of memory, you'll trigger what's essentially a segmentation fault because that memory doesn't exist. It will cause the chip to do a Power-up Clear (PUC), resetting the state of your processor. This is a tough error to debug.
How many addr bits?

## Slide 40: Assembly and Machine Languages
Instructions:
  words in a computers language
Instruction Set:
  the dictionary of the language
Assembly Language:
  human-readable format of computer instructions
Machine Language:
  computer-readable instructions - binary (1's and 0's)
Assembler
Assembly Language Program
Linker
Relocatable Object Code
Executable Code

## Slide 41: Let's write a MSP430 program
  Our chip version: Msp430g2553  open CCS
; This program sets all pins on Port 1 to output and high. Since LEDs 1 and 2 are connected to P1.0 and P1.6 respectively, they will light up. This program turns the LEDs on and off
.text
; turn off watchdog timer
main:
bis.b #0xFF, &P1DIR ; set port1 direction to output
Turn_on:
bis.b #0xFF, &P1OUT ; turn on leds at port1, bis?
; could of: move ____ , &P1OUT
Turn_off:
bic.b #0xFF, &P1OUT ; turn on leds at port1, bic?
; could of: move ____ , &P1OUT
jmp Turn_on ; loop forever
 what?
Stack pointer?

## Slide 42: Status register and Jumps
15 | 14 | 13 | 12 | 11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
Reserved |  |  |  |  |  |  | V | SCG1 | SCG0 | OSCOFF | CPUOFF | GIE | N | Z | C
Condition Code | Assembly Instruction | Description
000 | JNE/JNZ | Jump if Z==0 (if !=)
001 | JEQ/JZ | Jump if Z==1 (if ==)
010 | JNC/JLO | Jump if C==0 (if unsigned <)
011 | JC/JHS | Jump if C==1 (if unsigned >)
100 | JN | Jump if N==1 - Note there is no jump if N==0
101 | JGE | Jump if N==V (if signed >=)
110 | JL | Jump if N!=V (if signed <)
111 | JMP | Jump unconditionally