## Slide 1: ECE 382 Lesson 25
Lesson Outline
  Lab#4 lessons learned?
  Timers (like stopwatch, alarm, etc)
Admin
  Lab#4 Notebook/Bitbucket due COB

## Slide 2: Timer Block Diagram
0
1
2
3
4
5
clks
cnts
Family User Guide pp 357
Blue Book pp 46

## Slide 3: Timer (p 355 User’s Guide, BB p45)
0. Heart of the Timer: TAR
  16-bit Timer. How many clock ticks (cnts) till it rolls over?
  How do you read the Time in the TAR timer?
  Rising or Falling Edge?
  Clear? TACLR?
  RC? TAIFG?
  Where can you find these bits?

## Slide 4: Timer (p 370 User’s Guide, BB p 52)

## Slide 5: Timer Block Diagram
0
1
2
3
4
5
clks
cnts
Family User Guide pp 357
Blue Book pp 46

## Slide 6: Timer (p 370 User’s Guide, BB p 52)
1. TASSELx
  Selects one of 4 possible clocks to drive the timer
  TASSEL_2 // 2 means “10” mux select, or select SMCLK,
  // actually the binary number 0000 0010 0000 0000

## Slide 7: Timer Block Diagram
0
1
2
3
4
5
clks
cnts
Family User Guide pp 357
Blue Book pp 46

## Slide 8: Timer (p 370 User’s Guide, BB p 52)
2. IDx: Timer Prescalar
  Selects one of 4 possible clocks to drive the timer
IDx | Prescalar
00 | 1:1 or Divide by 1 ID_0
01 | 1:2 or Divide by 2 ID_1
10 | 1:4 or Divide by 4 ID_2
11 | 1:8 or Divide by 8 ID_3 so, a 1 MHz clock would become?

## Slide 9: Timer Block Diagram
0
1
2
3
4
5
clks
cnts
Family User Guide pp 357
Blue Book pp 46

## Slide 10: Timer (p 370 User’s Guide, BB p 52)
Mcx | Mode | Description
00 | Stop | The timer is halted. When should you use Stop mode? MC_0
01 | Up | The timer repeatedly counts from zero to the value of TACCR0. MC_1
10 | Continuous | The timer repeatedly counts from zero to 0FFFFh. MC_2
11 | Up/down | The timer repeatedly counts from zero up to the value of TACCR0 and back down to zero. MC_3
3. MCx - Count Mode

## Slide 11: Timer (p 358 User’s Guide, BB p 46)
Up Mode MC_1
  Counts from 0 to the value in register TACCR0. When it hits TACCR0, the CCIFG interrupt flag is set. When it hits 0 (the next tick), the TAIFG interrupt flag is set

## Slide 12: Timer (p 359 User’s Guide, BB p 47)
Continuous Mode MC_2
  Continuous mode counts from 0 to 0xffff. When it hits 0, the TAIFG interrupt flag is set

## Slide 13: Timer (p 360 User’s Guide, BB p 47)
Up / Down Mode MC_3
  Counts from 0 to the value in register TACCR0, then back down to 0. When it hits TACCR0, the CCIFG interrupt flag is set. When it hits 0, the TAIFG interrupt flag is set.

## Slide 14: MSP430G2553 Interrupt Vector Table
pp 11 of Device Specific
pp 109 of Blue Book

## Slide 15: Timer Block Diagram
0
1
2
3
4
5
clks
cnts
Family User Guide pp 357
Blue Book pp 46

## Slide 16: Example Code
Main.c
#include <msp430g2553.h>
void main(void) {
WDTCTL = WDTPW | WDTHOLD; // Stop watchdog timer
BCSCTL1 = CALBC1_8MHZ; // Set SMCLK 8 MHz
DCOCTL = CALDCO_8MHZ;
P1DIR = BIT6; // Set the green LED as an output
TACCR0 = 256 - 1; // Set the interval
TACTL &= ~TAIFG; // Clear any rollover flag
TACTL |= ID_0 | TASSEL_2 | MC_1; // Important Timer stuff!
while(1) {
while ((TACTL & TAIFG) == 0); // Polling timer flag? Would this be good for pong game?
TACTL &= ~TAIFG; // Clear rollover flag
P1OUT ^= BIT6; // toggle LED
} // end infinite loop
}
Notes: Let's examine what's going on here.
The first line of code moves r1 (the stack pointer) into r4. The compiler is using r4 as the frame pointer. When you call a function (main() in this case), all of its local variables are allocated on the stack. We call the space on the stack used by a function a stack frame. However, the stack pointer changes as you allocate more variables on the stack. So a variable that was at 4(r1) at one point in your function could later be at 8(r1) if the stack pointer changes. The frame pointer ensures a consistent address for the same variable throughout the function. If we store the address of the base of the stack frame in the frame pointer, each variable will always be stored at the same place relative to the frame pointer - so a variable at 4(r4) will always be accessible at 4(r4).
So the first line of code is setting the frame pointer. Next, the compiler adds 2 to the frame pointer. In most functions, the first thing you do is push the frame pointer onto the stack via push r4 - main is the exception. Adding two puts the base of the stack frame below this value, which is what we want.
Next, the compiler subtracts two from the stack pointer. This is because we're allocating our int variable on the stack, so we're giving it two bytes. If we allocated two ints, the compiler would subtract 4 from the stack pointer.
Our first four instructions are identical to our first sample program. We're setting up the frame pointer and allocating our variable on the stack.
Next, we're moving our variable into r15. Remember, our ABI says that the first parameter to a function should be passed in through r15 - so we move our there.
Next, we call the recursiveSummation subroutine the compiler has created.
Once inside the recursiveSummation subroutine, we push the framePointer onto the stack so we don't destroy it. Then, we establish a new frame pointer and allocate a variable on the stack - just like we did in main.
Next, the compiler moves the parameter we passed in r15 into the variable we established. It compares the variable to 1.
If it's greater than or equal to 1, we jump to .L3 - the label that holds the code in our else case. We move our parameter into r15 (the register that holds the first parameter we pass to functions), subtract one, and call our recursiveSummation subroutine again. This code is the recursiveSummation(numberToSum - 1) piece of our code. The final instruction adds the current parameter to the result passed back in r15. This code is the return numberToSum + piece of our code.
If it's less than 1, we're finished. We move 0 into r15, deallocate our variable from the stack, retrieve the frame pointer we pushed initially, and return.
If you're interested in learning more, check out this Wikipedia reading on the Call Stack.
After we're done, we'll add 2 to the stack pointer to deallocate int variable since we're done using it.

## Slide 17: In-Class Worksheet
To reduce confusion, let’s call the output of the mux associated with the TASSELx signal clks. Call the signal coming out of the IDx clock divider cnts.
A. Given: SMCLK = 8 MHz, TASSEL=2, ID=2, MC=1, TACCR0=0xECE, and TAR starts at 0
Find: How long will it take to roll over TAR? (Fill in the blanks)
clks
cnts

## Slide 18: In-Class Worksheet
To reduce confusion, let’s call the output of the mux associated with the TASSELx signal clks. Call the signal coming out of the IDx clock divider cnts.
A. Given: SMCLK = 8 MHz, TASSEL=2, ID=2, MC=1, TACCR0=0xECE, and TAR starts at 0
Find: How long will it take to roll over TAR? (Fill in the blanks)
clks
cnts

## Slide 19: In-Class Worksheet
To reduce confusion, let’s call the output of the mux associated with the TASSELx signal clks. Call the signal coming out of the IDx clock divider cnts.
B. Given : SMCLK = 8 MHz, TASSEL= 2, ID= 2, MC= 1, and TAR starts at 0
Find: The TACCR0 values that will roll over TAR in 84 μs?
clks
cnts

## Slide 20: In-Class Worksheet
To reduce confusion, let’s call the output of the mux associated with the TASSELx signal clks. Call the signal coming out of the IDx clock divider cnts.
B. Given : SMCLK = 8 MHz, TASSEL= 2, ID= 2, MC= 1, and TAR starts at 0
Find: The TACCR0 values that will roll over TAR in 84 μs?
clks
cnts

## Slide 21: In-Class Worksheet
To reduce confusion, let’s call the output of the mux associated with the TASSELx signal clks. Call the signal coming out of the IDx clock divider cnts.
Given an TAR=0, a 8Mhz clock, TASSEL_2, ID_2, MC_1,
and TACCR0=255, how long will it take to roll over TAR?
clks
cnts

## Slide 22: In-Class Worksheet
To reduce confusion, let’s call the output of the mux associated with the TASSELx signal clks. Call the signal coming out of the IDx clock divider cnts.
Given an TAR=0, a 8Mhz clock, TASSEL_2, ID_2, MC_1,
and TACCR0=255, how long will it take to roll over TAR?
  1 sec 4 clks 255 cnts
  ------------ * ------ * --------------- = 128 usec
  8 *10^6 clks 1 cnt 1 TAR roll over
clks
cnts

## Slide 23: In-Class Worksheet
To reduce confusion, let’s call the output of the mux associated with the TASSELx signal clks. Call the signal coming out of the IDx clock divider cnts.
Given an TAR=0, a 8Mhz clock, TASSEL_2, ID_0, MC_1
and TACCR0=2^16-1, how long will it take to roll over TAR?
clks
cnts

## Slide 24: In-Class Worksheet
To reduce confusion, let’s call the output of the mux associated with the TASSELx signal clks. Call the signal coming out of the IDx clock divider cnts.
Given an TAR=0, a 8Mhz clock, TASSEL_2, ID_0, MC_1
and TACCR0=2^16-1, how long will it take to roll over TAR?
  1 sec 1 clks 2^16-1 cnts
  ------------ * ------ * --------------- = 8.192 msec
  8 *10^6 clks 1 cnt 1 TAR roll over
clks
cnts

## Slide 25: In-Class Worksheet
To reduce confusion, let’s call the output of the mux associated with the TASSELx signal clks. Call the signal coming out of the IDx clock divider cnts.
Given an TAR=0, a 8Mhz clock, TASSEL_2, ID_0, MC_1
and TACCR0=2^16-1, how long will it take to roll over TAR?
3. Do the previous problem, except with ID_1.
clks
cnts

## Slide 26: In-Class Worksheet
To reduce confusion, let’s call the output of the mux associated with the TASSELx signal clks. Call the signal coming out of the IDx clock divider cnts.
Given an TAR=0, a 8Mhz clock, TASSEL_2, ID_0, MC_1
and TACCR0=2^16-1, how long will it take to roll over TAR?
3. Do the previous problem, except with ID_1.
  1 sec 2 clks 2^16 cnts
  ------------ * ------ * --------------- = 16.384 msec
  8 *10^6 clks 1 cnt 1 TAR roll over
clks
cnts

## Slide 27: In-Class Worksheet
To reduce confusion, let’s call the output of the mux associated with the TASSELx signal clks. Call the signal coming out of the IDx clock divider cnts.
Given an TAR=0, a 8Mhz clock, TASSEL_2, ID_0, MC_1
and TACCR0=2^16-1, how long will it take to roll over TAR?
4. Do the previous problem, except with ID_2.
clks
cnts

## Slide 28: In-Class Worksheet
To reduce confusion, let’s call the output of the mux associated with the TASSELx signal clks. Call the signal coming out of the IDx clock divider cnts.
Given an TAR=0, a 8Mhz clock, TASSEL_2, ID_0, MC_1
and TACCR0=2^16-1, how long will it take to roll over TAR?
4. Do the previous problem, except with ID_2.
  1 sec 4 clks 2^16 cnts
  ------------ * ------ * --------------- = 32.768 msec
  8 *10^6 clks 1 cnt 1 TAR roll over
clks
cnts

## Slide 29: In-Class Worksheet
To reduce confusion, let’s call the output of the mux associated with the TASSELx signal clks. Call the signal coming out of the IDx clock divider cnts.
Given an TAR=0, a 8Mhz clock, TASSEL_2, ID_0, MC_1
and TACCR0=2^16-1, how long will it take to roll over TAR?
5. Do the previous problem, except with ID_3.
clks
cnts

## Slide 30: In-Class Worksheet
To reduce confusion, let’s call the output of the mux associated with the TASSELx signal clks. Call the signal coming out of the IDx clock divider cnts.
Given an TAR=0, a 8Mhz clock, TASSEL_2, ID_0, MC_1
and TACCR0=2^16-1, how long will it take to roll over TAR?
5. Do the previous problem, except with ID_3.
  1 sec 8 clks 2^16 cnts
  ------------ * ------ * --------------- = 65.536 msec
  8 *10^6 clks 1 cnt 1 TAR roll over
clks
cnts

## Slide 31: In-Class Worksheet
To reduce confusion, let’s call the output of the mux associated with the TASSELx signal clks. Call the signal coming out of the IDx clock divider cnts.
Given an TAR=0, a 8Mhz clock, TASSEL_2, ID_1, and
MC_1, how many counts would it take to roll over TAR in
84us?
clks
cnts

## Slide 32: In-Class Worksheet
To reduce confusion, let’s call the output of the mux associated with the TASSELx signal clks. Call the signal coming out of the IDx clock divider cnts.
Given an TAR=0, a 8Mhz clock, TASSEL_2, ID_1, and
MC_1, how many counts would it take to roll over TAR in
84us?
8*10^6 clks 1 cnt 84uS
---------- * ------ * ------ = 336 counts
1 sec 2 clk
clks
cnts

## Slide 33: In-Class Worksheet
To reduce confusion, let’s call the output of the mux associated with the TASSELx signal clks. Call the signal coming out of the IDx clock divider cnts.
7. Complete the following table assuming SMCLK = 8 MHz, TASSEL= 2, MC= 1, TACCR0=0x2006, and TAR starts at 0. How long will it take to roll over TAR?
ID | Prescalar | MaxDelay (milliseconds)
0 | 1:1 | 
1 | 1:2 | 
2 | 1:4 | 
3 | 1:8 | 

## Slide 34: In-Class Worksheet
To reduce confusion, let’s call the output of the mux associated with the TASSELx signal clks. Call the signal coming out of the IDx clock divider cnts.
7. Complete the following table assuming SMCLK = 8 MHz, TASSEL= 2, MC= 1, TACCR0=0x2006, and TAR starts at 0. How long will it take to roll over TAR?
ID | Prescalar | MaxDelay (milliseconds)
0 | 1:1 | 
1 | 1:2 | 
2 | 1:4 | 
3 | 1:8 | 
ID | Prescalar | 
0 | 1:1 | 
1 | 1:2 | 
2 | 1:4 | 
3 | 1:8 | 

## Slide 35: In-Class Worksheet
To reduce confusion, let’s call the output of the mux associated with the TASSELx signal clks. Call the signal coming out of the IDx clock divider cnts.
8. Given SMCLK = 8 MHz, TASSEL= 2, MC_1, ID_2, provide a nice round number for TACCR0 that will cause TAR to roll over in 40 ms.
clks
cnts

## Slide 36: In-Class Worksheet
To reduce confusion, let’s call the output of the mux associated with the TASSELx signal clks. Call the signal coming out of the IDx clock divider cnts.
8. Given SMCLK = 8 MHz, TASSEL= 2, MC_1, ID_2, provide a nice round number for TACCR0 that will cause TAR to roll over in 40 ms.
clks
cnts

## Slide 37: In-Class Worksheet
To reduce confusion, let’s call the output of the mux associated with the TASSELx signal clks. Call the signal coming out of the IDx clock divider cnts.
9. Given these settings, how many counts will it take to create a delay of 550 μs? 1.65 ms? 4.5 ms? 90 ms?
clks
cnts

## Slide 38: In-Class Worksheet
To reduce confusion, let’s call the output of the mux associated with the TASSELx signal clks. Call the signal coming out of the IDx clock divider cnts.
9. Given these settings, how many counts will it take to create a delay of 550 μs? 1.65 ms? 4.5 ms? 90 ms?