## Slide 1: ECE 382 Lesson 3
ECE 382Website:
http://ece.ninja/382/index.html
Readings
  Debuggers MSP430 Instruction Set
Lesson Outline
  MSP430 Execution Model
  MSP430 Instruction Set
  Converting Assembly to Machine Code
Admin
  Skills Review due today!
  Assignment 1 due next lesson
  uCorrupt1 due next lesson

## Slide 2: MSP430’s ISA
Types of Instructions
    Single-operand
      SWPB r12
    Jump
      JMP loop
    Two-operand
      add r5, r6
      add src, dst
      dst = dst + src
      dst += src
    Three-operand?
      add r5, r6, r7

## Slide 3: MSP430’s ISA
Specifying values
    #10
      What's the # mean?
      What base is this number in?
    #0x10
      What base is this number in?
    #0b10
      What base is this number in?
    Assembler does the work of base conversion for you.
What is the process is to convert an assembly language program to an executable that we can load onto our chip?

## Slide 4: Assembly and Machine Languages
Instructions:
  words in a computers language
Instruction Set:
  the dictionary of the language
Assembly Language:
  human-readable format of computer instructions
Machine Language:
  computer-readable instructions - binary (1's and 0's)
Assembler
Assembly Language Program
Linker
Relocatable Object Code
Executable Code

## Slide 5: Steps for Translating and starting a program
Compiler
Assembler
Higher Level Language (HLL)
Assembly Language
Object File (Machine Code)
Linker
Executable
Loader
Memory
Object Files
Library Files

## Slide 6: MSP430’s ISA
Msp430g2553 Memory Map
512b of RAM - 0x200-0x400 16kb of ROM - 0xc000-0xffdf
0x1100-0xc000 is empty!
- There is no memory backing it up!
- If you attempt to write to this area of memory, you'll trigger what's essentially a segmentation fault because that memory doesn't exist. It will cause the chip to do a Power-up Clear (PUC), resetting the state of your processor. This is a tough error to debug.
How many addr bits?

## Slide 7: Let's write our first MSP430 program
; This program sets all pins on Port 1 to output and high. Since LEDs 1 and 2 are connected to P1.0 and P1.6 respectively, they will light up.
.include 'header.S'
.text
main:
mov.w #WDTPW, r15 ; turn off watchdog timer
xor.w #WDTHOLD, r15
mov.w r15, &WDTCTL
bis.b #0xFF, &P1DIR ; set port1 direction to output
bis.b #0xFF, &P1OUT ; turn on leds at port1
loop:
jmp loop ; loop forever

## Slide 8: Example Relocatable Code
Notice the addresses - the code starts at 0x0.
Hex dump of section '.text':
0x00000000 3f40005a 3fe08000 824f2001 f2d32200
0x00000010 f2d32100 b0120000 ff3f
After Linking
Notice the addresses - the code starts at 0xC000.
Hex dump of section '.text':
0x0000c000 3f40005a 3fe08000 824f2001 f2d32200
0x0000c010 f2d32100 b0121ac0 ff3fc243 21003041

## Slide 9: Example Dissassembled Code
Disassembly of section .text:
0000c000 <__ctors_end>:
c000: 3f 40 00 5a mov #23040, r15 ;#0x5a00
c004: 3f e0 80 00 xor #128, r15 ;#0x0080
c008: 82 4f 20 01 mov r15, &0x0120
c00c: f2 d3 22 00 bis.b #-1, &0x0022 ;r3 As==11
c010: f2 d3 21 00 bis.b #-1, &0x0021 ;r3 As==11
0000c014 <loop>:
c014: ff 3f jmp $+0 ;abs 0xc014

## Slide 10: MSP430 Instruction Set
  MSP430 Instruction Set
All instructions are 16 bits long. Their binary format looks like this:
15 | 14 | 13 | 12 | 11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
0 | 0 | 0 | 1 | 0 | 0 | Opcode |  |  | W=0/ B=1 | Ad |  | Dest reg |  |  | 
0 | 0 | 1 | Condition |  |  | PC offset (10 bit) |  |  |  |  |  |  |  |  | 
Opcode |  |  |  | Source reg |  |  |  | Ad | W=0/B=1 | As |  | Dest reg |  |  | 
:
Double-Operand (Format I)
Single-Operand (Format II)
Jumps (Format III)
Which row corresponds to each format?

## Slide 11: One Operand Instructions
:
Opcode | Assembly Instruction | Description
000 | RRC(.B) | 9-bit rotate right through carry. C->msbit->...->lsbit->C. Clear the carry bit beforehand to do a logical right shift.
001 | SWPB | Swap 8-bit register halves. No byte form.
010 | RRA(.B) | Badly named, this is an arithmetic right shift - meaning the most significant bit is preserved.
011 | SXT | Sign extend 8 bits to 16. No byte form.
100 | PUSH(.B) | Push operand on stack. Push byte decrements SP by 2. Most significant byte not overwritten. CPU BUG: PUSH #4 and PUSH #8 do not work when the short encoding using @r2 and @r2+ is used. The workaround, to use a 16-bit immediate, is trivial, so TI do not plan to fix this bug.
101 | CALL | Fetch operand, push PC, then assign operand value to PC. Note the immediate form is the most commonly used. There is no easy way to perform a PC-relative call; the PC-relative addressing mode fetches a word and uses it as an absolute address. This has no byte form.
110 | RETI | Pop SR, then pop PC. Note that because flags like CPUOFF are in the stored status register, the CPU will normally return to the low-power mode it was previously in. This can be changed by adjusting the SR value stored on the stack before invoking RETI (see below). The operand field is unused.
111 | Unused | 

## Slide 12: Relative Jumps
:
Condition Code | Assembly Instruction | Description
000 | JNE/JNZ | Jump if Z==0 (if !=)
001 | JEQ/Z | Jump if Z==1 (if ==)
010 | JNC/JLO | Jump if C==0 (if unsigned <)
011 | JC/JHS | Jump if C==1 (if unsigned >)
100 | JN | Jump if N==1 - Note there is no jump if N==0
101 | JGE | Jump if N==V (if signed >=)
110 | JL | Jump if N!=V (if signed <)
111 | JMP | Jump unconditionally

## Slide 13: Two Operand Instructions
:
These are generally of the form OP src, dst which actually means dest = src OP dest.
Opcode | Assembly Instruction | Description | Notes
0100 | MOV src, dest | dest = src | The status flags are NOT set.
0101 | ADD src, dest | dest += src | 
0110 | ADDC src, dest | dest += src + C | 
0111 | SUBC src, dest | dest += ~src + C | 
1000 | SUB src, dest | dest -= src | Implemented as dest += ~src + 1
1001 | CMP src, dest | dest - src | Sets status only; the destination is not written.
1010 | DADD src, dest | dest += src + C, BCD (Binary Coded Decimal) | 
1011 | BIT src, dest | dest & src | Sets status only; the destination is not written.
1100 | BIC src, dest | dest &= ~src | The status flags are NOT set.
1101 | BIS src, dest | dest ¦=src | The status flags are NOT set.
1110 | XOR src, dest | dest ^= src | 
1111 | AND src, dest | dest &= src | 

## Slide 14: Emulated Instructions
:
Emulated Instruction | Assembly Instruction | Notes
NOP | MOV r3, r3 | 
POP dst | MOV @SP+, dst | 
BR dst | MOV dst, PC | BR dst
RET | MOV @SP+, PC | RET
CLRC | BIC #1, SR | 
SETC | BIS #1, SR | 
CLRZ | BIC #2, SR | 
SETZ | BIS #2, SR | 
CLRN | BIC #4, SR | 
SETN | BIS #4, SR | 
DINT | BIC #8, SR | 
EINT | BIS #8, SR | 

## Slide 15: More Emulated Instructions
:
Emulated Instruction | Assembly Instruction
RLA(.B) | ADD(.B) dst, dst
RLC(.B) | ADDC(.B) dst, dst
INV(.B) dst | XOR(.B) #-1, dst
CLR(.B) dst | MOV(.B) #0, dst
TST(.B) dst | CMP(.B) #0, dst
DEC(.B) dst | SUB(.B) #1, dst
DECD(.B) dst | SUB(.B) #2, dst
INC(.B) dst | ADD(.B) #1, dst
INCD(.B) dst | ADD(.B) #2, dst
ADC(.B) dst | ADDC(.B) #0, dst
DADC(.B) dst | DADD(.B) #0, dst
SBC(.B) dst | SUBC(.B) #0, dst

## Slide 16: Let's write a MSP430 program
  Our chip version: Msp430g2553  open CCS
; This program sets all pins on Port 1 to output and high. Since LEDs 1 and 2 are connected to P1.0 and P1.6 respectively, they will light up. This program turns the LEDs on and off
.text
; turning off watchdog timer NOT shown
main:
bis.b #0xFF, &P1DIR ; set port1 direction to output
Turn_on:
bis.b #0xFF, &P1OUT ; turn on leds at port1, bis?
; alternatively: mov ____ , &P1OUT ???
Turn_off:
bic.b #0xFF, &P1OUT ; turn on leds at port1, bic?
; alternatively: mov ____ , &P1OUT ???
jmp Turn_on ; loop forever
 what?
Stack pointer?

## Slide 17: Debugging Example Using breakpoints
; example program to add the numbers 10+9+8+...+1 and put result into 0x0200
mov.w #10, r6
mov.w #0, r5
summation: add.w r6, r5
dec r6
jnz summation
mov.w r5, &0x0200
forever: jmp forever

## Slide 18: Sample Program
repeat:
mov.b #0x75, r10
add.b #0xC7, r10
;result should be 0x13c, so we should see 3c in r10 and carry bit set
adc r10 ;since carry bit was set, this should increment r10 to 3d
inv.b r10 ;invert, so r10 should be c2
mov.w #0x00aa, r10
sxt r10 ;sign extend should clear upper 8 bits
inv r10
swpb r10
mov.w r10, r9
jmp repeat
c010: 7a 40 75 00 mov.b #117, r10 ;#0x0075
c014: 7a 50 c7 00 add.b #199, r10 ;#0x00c7
c018: 0a 63 adc r10
c01a: 7a e3 xor.b #-1, r10 ;r3 As==11
c01c: 3a 40 aa 00 mov #170, r10 ;#0x00aa
c020: 8a 11 sxt r10
c022: 3a e3 inv r10
c024: 8a 10 swpb r10
c026: 09 4a mov r10, r9
c028: f3 3f jmp $-24 ;abs 0xc010
Hex
Decimal

## Slide 19: Sample Program
c010: 7a 40 75 00 mov.b #117, r10 ;#0x0075
c014: 7a 50 c7 00 add.b #199, r10 ;#0x00c7
c018: 0a 63 adc r10
c01a: 7a e3 xor.b #-1, r10 ;r3 As==11
c01c: 3a 40 aa 00 mov #170, r10 ;#0x00aa
c020: 8a 11 sxt r10
c022: 3a e3 inv r10
c024: 8a 10 swpb r10
c026: 09 4a mov r10, r9
c028: f3 3f jmp $-24 ;abs 0xc010
1
2
4
3

## Slide 20: MSP430 Instruction Set
  MSP430 Instruction Set
All instructions are 16 bits long. Their binary format looks like this:
15 | 14 | 13 | 12 | 11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
0 | 0 | 0 | 1 | 0 | 0 | Opcode |  |  | W=0/ B=1 | Ad |  | Dest reg |  |  | 
0 | 0 | 1 | Condition |  |  | PC offset (10 bit) |  |  |  |  |  |  |  |  | 
Opcode |  |  |  | Source reg |  |  |  | Ad | W=0/B=1 | As |  | Dest reg |  |  | 
:
Double-Operand (Format I)
Single-Operand (Format II)
Jumps (Format III)

## Slide 21: Single-Operand Instruction
  SXT r10
All instructions are 16 bits long. Their binary format looks like this:
15 | 14 | 13 | 12 | 11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
0 | 0 | 0 | 1 | 0 | 0 | Opcode |  |  | W=0/ B=1 | Ad |  | Dest reg |  |  | 
:

## Slide 22: Single-Operand Instruction
All instructions are 16 bits long. Their binary format looks like this:
:
SXT r10
_ _ _ _ _ _ _ _ _ _ _ _ _ _ _ _
register mode
Table 3-3 Blue Book Pg 12
no .b
Figure 3-12
Family User Guide 3.4.5 pp62
Blue Book pp19

## Slide 23: Core Instruction Map
Figure 3-12
Family User Guide 3.4.5 pp62
Blue Book pp19

## Slide 24: Sample Program
repeat:
mov.b #0x75, r10
add.b #0xC7, r10
;result should be 0x13c, so we should see 3c in r10 and carry bit set
adc r10
;since carry bit was set, this should increment r10 to 3d
inv.b r10
;invert, so r10 should be c2
mov.w #0x00aa, r10
sxt r10
;sign extend should clear upper 8 bits
inv r10
swpb r10
mov.w r10, r9
jmp repeat
c010: 7a 40 75 00 mov.b #117, r10 ;#0x0075
c014: 7a 50 c7 00 add.b #199, r10 ;#0x00c7
c018: 0a 63 adc r10
c01a: 7a e3 xor.b #-1, r10 ;r3 As==11
c01c: 3a 40 aa 00 mov #170, r10 ;#0x00aa
c020: 8a 11 sxt r10
c022: 3a e3 inv r10
c024: 8a 10 swpb r10
c026: 09 4a mov r10, r9
c028: f3 3f jmp $-24 ;abs 0xc010
PCOLD
PCNEW
PCNEW - PCOLD

## Slide 25: Relative Jumps
:
Condition Code | Assembly Instruction | Description
000 | JNE/JNZ | Jump if Z==0 (if !=)
001 | JEQ/Z | Jump if Z==1 (if ==)
010 | JNC/JLO | Jump if C==0 (if unsigned <)
011 | JC/JHS | Jump if C==1 (if unsigned >)
100 | JN | Jump if N==1 - Note there is no jump if N==0
101 | JGE | Jump if N==V (if signed >=)
110 | JL | Jump if N!=V (if signed <)
111 | JMP | Jump unconditionally
How many bits do we have for offset in a jump?
What is the range of signed numbers?
Not directly found in datasheets!

## Slide 26: Relative Jump Instruction
  JMP $-024
All instructions are 16 bits long. Their binary format looks like this:
15 | 14 | 13 | 12 | 11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
0 | 0 | 1 | Condition |  |  | PC offset (10 bit) |  |  |  |  |  |  |  |  | 
:
Family User Guide 3.4.5 pp59
Blue Book pp18
Figure 3-12
Family User Guide 3.4.5 pp62
Blue Book pp19
_ _ _ _ _ _ _ _ _ _ _ _ _ _ _ _

## Slide 27: Sample Program
repeat:
mov.b #0x75, r10
add.b #0xC7, r10
;result should be 0x13c, so we should see 3c in r10 and carry bit set
adc r10
;since carry bit was set, this should increment r10 to 3d
inv.b r10
;invert, so r10 should be c2
mov.w #0x00aa, r10
sxt r10
;sign extend should clear upper 8 bits
inv r10
swpb r10
mov.w r10, r9
jmp repeat
c010: 7a 40 75 00 mov.b #117, r10 ;#0x0075
c014: 7a 50 c7 00 add.b #199, r10 ;#0x00c7
c018: 0a 63 adc r10
c01a: 7a e3 xor.b #-1, r10 ;r3 As==11
c01c: 3a 40 aa 00 mov #170, r10 ;#0x00aa
c020: 8a 11 sxt r10
c022: 3a e3 inv r10
c024: 8a 10 swpb r10
c026: 09 4a mov r10, r9
c028: f3 3f jmp $-24 ;abs 0xc010

## Slide 28: Two-Operand Instruction - Practice
All instructions are 16 bits long. Their binary format looks like this:
:
MOV r10, r9
 | 15 | 14 | 13 | 12 | 11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
Two Operand | Opcode |  |  |  | Source reg |  |  |  | Ad | W=0/B=1 | As |  | Dest reg |  |  | 
_ _ _ _ _ _ _ _ _ _ _ _ _ _ _ _
register mode
register mode
no .b

## Slide 29: Two-Operand Instruction with Immediate
All instructions are 16 bits long. Their binary format looks like this:
15 | 14 | 13 | 12 |  | 11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
Opcode |  |  |  |  | Source reg |  |  |  | Ad | W=0/B=1 | As |  | Dest reg |  |  | 
Source or Destination 15:0 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Destination 15:0 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
:
add.b #0xC7, r10
Figure 3-12
Family User Guide 3.4.5 pp62
Blue Book pp19
Register mode = Immediate
As/Ad 11/-
***Immediate mode so Source is the PC (i.e. 0000)
yes .b
_ _ _ _ _ _ _ _ _ _ _ _ _ _ _ _
????
Notes: The source and destination of an instruction are defined by the following fields:
src The source operand defined by As and S-reg
dst The destination operand defined by Ad and D-reg
As The addressing bits responsible for the addressing mode used for the source (src)
S-reg The working register used for the source (src)
Ad The addressing bits responsible for the addressing mode used for the destination (dst)
D-reg The working register used for the destination (dst)
B/W Byte or word operation:
0: word operation
1: byte operation

## Slide 30: MSP430 addressing modes
As/Ad | Addressing Mode | Description | Example
00/0 | Rn | Register direct | mov r8, r9
01/1 | offset(Rn) | Indexed | mov 2(r8), r9
10/- | @Rn | Register indirect | mov @r8, r9
11/- | @Rn+ | Register indirect with post-increment | mov @r8+, r9
01/1 | ADDR | Symbolic (PC relative) | mov LoopCtr, r6
01/1 | &ADDR | Absolute | mov r5, &0x0200
11/- | #N | Immediate | mov #0x2006, r6
Table 3-3 Blue Book Pg 12

## Slide 31: Next Lesson: addressing modes
Code | Addressing Mode | Description
00 | Rn | Register direct
01 | offset(Rn) | Register indexed
10 | @Rn | Register indirect
11 | @Rn+ | Register indirect with post-increment

## Slide 32: MSP430’s ISA
Msp430g2553 Memory Map
512b of RAM - 0x200-0x400 16kb of ROM - 0xc000-0xffdf
0x1100-0xc000 is empty!
- There is no memory backing it up!
- If you attempt to write to this area of memory, you'll trigger what's essentially a segmentation fault because that memory doesn't exist. It will cause the chip to do a Power-up Clear (PUC), resetting the state of your processor. This is a tough error to debug.
How many addr bits?