## Slide 1: ECE 382 Lesson 2
Readings
  Assembler Linker
Lesson Outline
  Intro to the MSP430
  MSP430 Architecture
  Assembly and Machine Languages
Admin
  Skills Review due next time!

## Slide 2: Feedback Forms 2016
What you want me to do?
  Clearly explain the learning goals/objectives for every lesson: What is the focal point of each lesson, Make expectation clear from the start
  Stay on track with the lessons, encourage further exploration
  Discuss practical application and examples,
  Be able to explain in a different way if I am not getting it
  Be available for help, Be available for EI often, Be around for EI, Be available for EI (within reason). Always have and open door for EI, Be available for EI on T-Days
  Be prepared to see me all the time in your office
  Be patient with me – I went through a bit of EI in 281
  Lots of EI hours. Really, really dumb down lab/project instructions  Last year never could understand what it was asking for in 281, Always have an open door for EI and understand if some of us are completely lost
  Try to prep us for GRs, Review for GRs!
  Teach what will be on the test/provide a way to know what will be on the test
  Be real and understanding. If we have no excuse to not do better let us know, but if we voice a problem, please listen and try to understand.
  The chicken dance
  Teach, test us on what we’ve been taught, helpful EI, Teach!

## Slide 3: Feedback Forms 2015
What you want me to do?
  Be able to explain things multiple ways
  Be willing to break down concepts in EI, I might be by a lot
  War stories, videos
  Work through examples in class like the GR/Labs
  Keep it interesting
  Teach! Teach well
  Be specific about what you want from us
  Be inviting to students coming into EI
  Have Fun in class
  Teach well and make material understandable
  Teach me what I need to know for graded assignments
  More interactive in-class work
  Provide better info about what you want in labs
  Go over labs thoroughly
  Help me to further my understanding of Comp Eng and the Air Force
  Grade easy
  Go over what topics/terms will be on GRs

## Slide 4: Feedback Forms 2016
What do you want from the class?
  A deeper understanding of computer systems
  In need to figure out interrupts especially
  To not be overwhelmed
  Interesting projects that won’t make me hate ECE
  I’d like to understand what embedded systems are since I have no idea
  To expand knowldege of how a computer operates on a lower level, Knowledge
  A greater appreciation for some really cool robotics
  Learn some appreciation (that I can understand)
  Better understanding of coding, Learn and understand the material, To get better with assembly, Higher understanding of computer systems, learning to code better
  Know more about programming in general; not just specifics for one project
  Further my skills – understand information
  An okay grade
  Better under understanding of MIPS &other systems and how they use basic programs
  Learn course material
  A better understanding of electronics and how this stuff applies to our lives
  Learning how to mess with microcontrollers in personal projects.

## Slide 5: Feedback Forms 2015
What do you want from the class?
  Not much HW? Hopefully.
  A better understanding of Assembly and how to use it
  Knowledge
  Understand coding microcontroller better
  Establish a better comp eng and coding background
  Learn! , Learn cool ECE stuff, To learn and pass, to pass
  To have fun
  Further my skills, Real-world application skills
  Reasonable work load
  Be comfortable enough to use microcontrollers on my own
  Learn something practical
  Better understanding of the design of embedded system and their advantages over computers
  Be interactive. It’s easier to learn with the class involved
  To get to the point that I can do my own projects with Embedded systems
  Better understanding of assembly
  An A 

## Slide 6: Feedback Forms 2015
What you have heard about this class?
  I have not heard anything about this class, Nothing, Not much
  Everything
  Harder than 281, It’s as hard as 281
  Harder than 281, hardest class in CNS
  Fire and Brimstone. (Just kidding, but I get that it’s a tough class that one needs to put a lot of work into)
  Hard, but last computer class for EEs
  Challenging; hardest class taken here
  So rough…I should set up a small bed in the lab because I will be there a lot
  Very hard
  Hard, lots of work
  Challenging
  It’s a lot of work
  Beware!
  N/A
  It’s Horrible – worse than 281
  Lots of work, esp. after prog…not hard conceptually

## Slide 7: Feedback Forms 2015
What you have heard about this class?
  Nothing really
  Not much, just basing ideas off of 281 last year
  Nothing, better than 281 (or similar to 281)
  Its Fun!
  It’s part of my major
  Build a robot
  Awful
  Not good things, also not horrible things
  Good/interesting material, but its hard
  Fairly difficult class, lots of assembly but interesting/fun
  Knowledge
  That it’s great!
  Nothing but vhdl style work (We aren’t doing vhdl this semester)

## Slide 8: Intro to the MSP430
The MSP430 is an industry leader in low-cost, low-power consumption embedded applications
  RISC architecture with just 27 instructions.
  Products in the Wild Using MSP430
  Only $5
  Our version: Msp430g2553
What is an ISA?

## Slide 9: Instruction Set Architecture
Consists of
  set of operations (instructions)
  registers
  data units (byte/word/etc)
  addressing modes
  memory organization / memory map

## Slide 10: MSP430’s ISA
RISC architecture
  fewer instructions (27)
  emulates higher-level instructions (about 27)
    for instance, NOP  ___________
  16-bit datapath
    What is a datapath?

## Slide 11: MSP430’s ISA
  16-bit datapath
    word size is 16 bits
    word is the natural unit of info for the processor
      16 bit addresses
      16 bit registers
      all instructions are 16 bits long
      this consistency isn't necessarily true of all processors, but it's convenient - allows us to load addresses into registers, perform ops on them, etc.
What is a register?

## Slide 12: MSP430’s ISA
Registers - 16 bits wide
  Fast memory that holds values in-use by the CPU
  Four special purpose registers
    r0 - Program Counter - holds address of instruction currently being executed
    r1 - Stack Pointer - address of top of stack
    r2 - Status Register - holds flags related to various conditions
    r3 - Constant Generator - 0, but can assume other values for different addressing modes (L4)
  12 general purpose registers
    r4 to r15: can be used to hold anything you want

## Slide 13: MSP430’s ISA
Set of Operations
  27 Instructions in 3 families - we'll talk about these next time
    Single-operand
      for instance, SWPB r12
    Conditional jump
      for instance, JMP jump_label
    Two-operand
      for instance, MOV r12, r10

## Slide 14: MSP430’s ISA
Data Units
  byte-addressable memory
  instructions for byte and word actions
    MOV.B r12, r10
    MOV.W r12, r10
  remember, word size is 16 bits
    words must lie on even addresses

## Slide 15: MSP430’s ISA
Msp430g2553 Memory Map
512b of RAM - 0x200-0x400 16kb of ROM - 0xc000-0xffdf
0x1100-0xbfff is empty!
- There is no memory backing it up!
- If you attempt to write to this area of memory, you'll trigger what's essentially a segmentation fault because that memory doesn't exist. It will cause the chip to do a Power-up Clear (PUC), resetting the state of your processor. This is a tough error to debug.
How many addr bits?
 |  | MSP430G2553
Memory Main: interrupt vector Main: code memory | Size Flash Flash | 16kB 0xFFFF to 0xFFC0 0xFFFF to 0xC000
Information memory | Size Flash | 256 Byte 010FFh to 01000h
RAM | Size | 512 Byte 0x03FF to 0x0200
Peripherals | 16-bit 8-bit 8-bit SFR | 01FFh to 0100h 0FFh to 010h 0Fh to 00h
Excerpt from Table 8: Memory Organization from MSP430G2x53 Device Specific User Guide (pp13) |  | 

## Slide 16: Big/Little Endian Byte Storage
There are two storage conventions: big endian and little endian
The value ABCD1234H would be stored as shown below for the different storage conventions
The name big/little endian answers the question: “What is stored in Byte #0?”
Byte zero holds Big Endian of the word
Byte zero holds Little Endian of the word
0
1
0
0
0
0
1
0
Byte #1
0
0
1
1
0
0
0
1
Low Order Byte
(Byte #0)
1
1
0
1
1
1
0
0
Byte #2
1
0
1
1
1
1
0
1
Byte #1
1
0
1
0
1
1
0
0
Low Order Byte
(Byte #0)
0
0
1
0
0
1
0
0
High Order Byte
(Byte #3)
0
0
0
1
0
0
1
1
Byte #2
(12)
(34)
1
0
1
1
High Order Byte
(Byte #3)
1
0
1
0
(AB)
(CD)
(CD)
(AB)
(34)
(12)

## Slide 17: MSP430Architecture Uses Little Endian
Values stored in little-endian byte order
Least significant byte is stored first
5000
5001
5002
5003

## Slide 18: MSP430’s ISA
Endianness
  concerned with the ordering of bytes on a computer.
  Little Endian means the least significant byte of a chunk of data is stored at the lowest memory address.
    MSP430 and your x86_64 are little endian
  Big Endian means the most significant byte of a chunk of data is stored at the lowest memory address.
    The 68S12 used in previous classes used this
If we executed MOV.W #0xdfec, &0x0200, how would that word be stored in memory?
addr | value
200 | 
201 | 
202 | 
203 | 
Debugger: 200

## Slide 19: Assembly and Machine Languages
Instructions:
  words in a computers language
Instruction Set:
  the dictionary of the language
Assembly Language:
  human-readable format of computer instructions
Machine Language:
  computer-readable instructions - binary (1's and 0's)
Assembler
Assembly Language Program
Linker
Relocatable Object Code
Executable Code

## Slide 20: Steps for Translating and starting a program
Compiler
Assembler
Higher Level Language (HLL)
Assembly Language
Object File (Machine Code)
Linker
Executable
Loader
Memory
Object Files
Library Files

## Slide 21: Let's write our first MSP430 program
; This program sets all pins on Port 1 to output and high. Since LEDs 1 and 2 are connected to P1.0 and P1.6 respectively, they will light up.
.include 'header.S'
.text
main:
mov.w #WDTPW, r15 ; turn off watchdog timer
xor.w #WDTHOLD, r15
mov.w r15, &WDTCTL
bis.b #0xFF, &P1DIR ; set port1 direction to output
bis.b #0xFF, &P1OUT ; turn on leds at port1
loop:
jmp loop ; loop forever

## Slide 22: Example Relocatable Code
Notice the addresses - the code starts at 0x0.
Hex dump of section '.text':
0x00000000 3f40005a 3fe08000 824f2001 f2d32200
0x00000010 f2d32100 b0120000 ff3f
After Linking
Notice the addresses - the code starts at 0xC000.
Hex dump of section '.text':
0x0000c000 3f40005a 3fe08000 824f2001 f2d32200
0x0000c010 f2d32100 b0121ac0 ff3fc243 21003041

## Slide 23: Example Dissassembled Code
Disassembly of section .text:
0000c000 <__ctors_end>:
c000: 3f 40 00 5a mov #23040, r15 ;#0x5a00
c004: 3f e0 80 00 xor #128, r15 ;#0x0080
c008: 82 4f 20 01 mov r15, &0x0120
c00c: f2 d3 22 00 bis.b #-1, &0x0022 ;r3 As==11
c010: f2 d3 21 00 bis.b #-1, &0x0021 ;r3 As==11
0000c014 <loop>:
c014: ff 3f jmp $+0 ;abs 0xc014

## Slide 24
Code Composer Studio demo…