## Slide 1: ECE 382 Lesson 22
Readings
  Mapping C Programming Constructs to MSP430 Assembly
Lesson Outline
  Writing Clean Code
  Mapping C to Assembly
  Calling Assembly from C
  Lab#4 Intro
Admin
  Assignment 8 due BOC next today
  Lab#4 Prelab due BOC next lesson

## Slide 2: Writing Clean Code
Meaningful Names
Use intention-revealing names ("self-documenting")
  int d, temp; // elapsed time in days, a temporary variable
  int elapsedTimeInDays, daysSinceModification;
Make meaningful distinctions
  void copyChars(char* a1, char* a2)
  void copyChars(char* source, char* destination)
Use pronounceable names
  DtaRcrd
  DataRecord
Use searchable names
  MAX
  MAX_STUDENTS
Functions: use verbs!
  forward()
  moveForward()
Don't be cute
  holyHandGrenade()
  deleteItem()
Pick one word per concept
  Bad: fetch(), retrieve(), get()
Okay to use i, j, k for loop counters

## Slide 3: Clean Functions
Small - ideally less than 10 lines long
Do one thing
Use descriptive names
Parameters: rarely need more than two or three
Side effects - function should only do what you say it does
Do not use static or global variables
Only depend on local variables / parameters
Don't repeat yourself - write a function instead of copy / paste
Only one entry / exit point
Indent correctly!

## Slide 4: Clean Comments
Comment on "big picture" items
  Head of each file
  Definition of each function
  Beginning of each major block of code
As you move deeper in the hierarchy, the comments are more specific
Try writing functions / meaningful names
  if ((employeeFlags & HOURLY_FLAGS) && (employeeAge > 65)) ...
  if (isEligibleForFullBenefits(employee)) ...
TODO comments
  // TODO: Make this into a function
  // TODO: Write new header file to group these functions
Bad comments
  Restating your code (a = 1; // Setting a to 1)
  Commented-Out code
  Too much information
  Don't comment bad code - rewrite it.

## Slide 5: Mapping C to Assembly
Assembly Version:
bis.b #BIT0|BIT6, &P1DIR
bic.b #BIT3, &P1DIR
bis.b #BIT3, &P1REN
bis.b #BIT3, &P1OUT
check_btn: bit.b #BIT3, &P1IN
jz set_lights
bic.b #BIT0|BIT6, &P1OUT
jmp check_btn
set_lights: bis.b #BIT0|BIT6, &P1OUT
jmp check_btn
C Version:
#include <msp430g2553.h>
#define TRUE 1
void main(void)
{
P1DIR |= BIT0|BIT6;
P1DIR &= ~BIT3;
P1REN |= BIT3;
P1OUT |= BIT3;
while (TRUE)
{
if (P1IN & BIT3)
P1OUT &= ~(BIT0|BIT6);
else
P1OUT |= BIT0|BIT6;
}
}

## Slide 6: Mapping C to Assembly
C Version:
#include <msp430g2553.h>
Typedef unsigned short int16;
int16 func(int16 w, int16 x, int16 y, int16 z);
void main() {
Int16 a,b,c,d,e;
a=1;b=2;c=3;d=4;
while(1) {
e = func(a,b,c,d);
}
}
int16 func(int16 w, int16 x, int16 y, int16 z) {
int16 sum;
sum = w+x+y+z;
return(sum);
}
Generated Assembly Code:
11 e = func(a,b,c,d);
$C$L1:
c074: MOV.W @SP,R12
c076: MOV.W 0x0002(SP),R13
c07a: MOV.W 0x0004(SP),R14
c07e: MOV.W 0x0006(SP),R15
c082: CALL #func
c086: MOV.W R12,0x0008(SP)
10 while(1) {
c08a: JMP ($C$L1)
int16 func(int16 w, int16 x,
int16 y, int16 z) {
func():
c08c: SUB.W #0x000a,SP
c090: MOV.W R15,0x0006(SP)
c094: MOV.W R14,0x0004(SP)
c098: MOV.W R13,0x0002(SP)
c09c: MOV.W R12,0x0000(SP)
17 sum = w+x+y+z;
c0a0: MOV.W R13,R12
c0a2: ADD.W @SP,R12
c0a4: ADD.W 0x0004(SP),R12
c0a8: ADD.W 0x0006(SP),R12
c0ac: MOV.W R12,0x0008(SP)
19 }
c0b0: ADD.W #0x000a,SP
c0b4: RET
Notes: Let's examine what's going on here.
The first line of code moves r1 (the stack pointer) into r4. The compiler is using r4 as the frame pointer. When you call a function (main() in this case), all of its local variables are allocated on the stack. We call the space on the stack used by a function a stack frame. However, the stack pointer changes as you allocate more variables on the stack. So a variable that was at 4(r1) at one point in your function could later be at 8(r1) if the stack pointer changes. The frame pointer ensures a consistent address for the same variable throughout the function. If we store the address of the base of the stack frame in the frame pointer, each variable will always be stored at the same place relative to the frame pointer - so a variable at 4(r4) will always be accessible at 4(r4).
So the first line of code is setting the frame pointer. Next, the compiler adds 2 to the frame pointer. In most functions, the first thing you do is push the frame pointer onto the stack via push r4 - main is the exception. Adding two puts the base of the stack frame below this value, which is what we want.
Next, the compiler subtracts two from the stack pointer. This is because we're allocating our int variable on the stack, so we're giving it two bytes. If we allocated two ints, the compiler would subtract 4 from the stack pointer.
Our first four instructions are identical to our first sample program. We're setting up the frame pointer and allocating our variable on the stack.
Next, we're moving our variable into r15. Remember, our ABI says that the first parameter to a function should be passed in through r15 - so we move our there.
Next, we call the recursiveSummation subroutine the compiler has created.
Once inside the recursiveSummation subroutine, we push the framePointer onto the stack so we don't destroy it. Then, we establish a new frame pointer and allocate a variable on the stack - just like we did in main.
Next, the compiler moves the parameter we passed in r15 into the variable we established. It compares the variable to 1.
If it's greater than or equal to 1, we jump to .L3 - the label that holds the code in our else case. We move our parameter into r15 (the register that holds the first parameter we pass to functions), subtract one, and call our recursiveSummation subroutine again. This code is the recursiveSummation(numberToSum - 1) piece of our code. The final instruction adds the current parameter to the result passed back in r15. This code is the return numberToSum + piece of our code.
If it's less than 1, we're finished. We move 0 into r15, deallocate our variable from the stack, retrieve the frame pointer we pushed initially, and return.
If you're interested in learning more, check out this Wikipedia reading on the Call Stack.
After we're done, we'll add 2 to the stack pointer to deallocate int variable since we're done using it.

## Slide 7: Calling Assembly Functions from C
For our compiler, it follows the this convention for passing parameters when calling an assembly function from C
First input | R12
Second input | R13
Third input | R14
Fourth input | R15
Fifth and beyond | Stack
return | R12

## Slide 8: Example Calling Assembly from C
Main.c
#include <msp430g2553.h>
typedef unsigned short int16;
extern int16 func(int16 w, int16 x, int16 y, int16 z); /* Function Prototype for asm function */
void main(void) {
int16 a,b,c,d;
WDTCTL=WDTPW+WDTHOLD; /* stop WD */
a=1; b=2; c=3; d=4;
while(1) {
b = func(a,b,c,d);
}
}
math.asm
.cdecls C,LIST,"msp430.h"
.text
.retain
.retainrefs
.global func
func: ; implement sum = w+x+y+z;
add R13, R12 ; r12 = w [r12] + x [r13]
add R14, R12 ; r12 = y [r14] + (w+x) [r12]
add R15, R12 ; r12 = z [r15] + (w+x+y) [r12]
ret ; r12 is return parameter (sum)
Notes: Let's examine what's going on here.
The first line of code moves r1 (the stack pointer) into r4. The compiler is using r4 as the frame pointer. When you call a function (main() in this case), all of its local variables are allocated on the stack. We call the space on the stack used by a function a stack frame. However, the stack pointer changes as you allocate more variables on the stack. So a variable that was at 4(r1) at one point in your function could later be at 8(r1) if the stack pointer changes. The frame pointer ensures a consistent address for the same variable throughout the function. If we store the address of the base of the stack frame in the frame pointer, each variable will always be stored at the same place relative to the frame pointer - so a variable at 4(r4) will always be accessible at 4(r4).
So the first line of code is setting the frame pointer. Next, the compiler adds 2 to the frame pointer. In most functions, the first thing you do is push the frame pointer onto the stack via push r4 - main is the exception. Adding two puts the base of the stack frame below this value, which is what we want.
Next, the compiler subtracts two from the stack pointer. This is because we're allocating our int variable on the stack, so we're giving it two bytes. If we allocated two ints, the compiler would subtract 4 from the stack pointer.
Our first four instructions are identical to our first sample program. We're setting up the frame pointer and allocating our variable on the stack.
Next, we're moving our variable into r15. Remember, our ABI says that the first parameter to a function should be passed in through r15 - so we move our there.
Next, we call the recursiveSummation subroutine the compiler has created.
Once inside the recursiveSummation subroutine, we push the framePointer onto the stack so we don't destroy it. Then, we establish a new frame pointer and allocate a variable on the stack - just like we did in main.
Next, the compiler moves the parameter we passed in r15 into the variable we established. It compares the variable to 1.
If it's greater than or equal to 1, we jump to .L3 - the label that holds the code in our else case. We move our parameter into r15 (the register that holds the first parameter we pass to functions), subtract one, and call our recursiveSummation subroutine again. This code is the recursiveSummation(numberToSum - 1) piece of our code. The final instruction adds the current parameter to the result passed back in r15. This code is the return numberToSum + piece of our code.
If it's less than 1, we're finished. We move 0 into r15, deallocate our variable from the stack, retrieve the frame pointer we pushed initially, and return.
If you're interested in learning more, check out this Wikipedia reading on the Call Stack.
After we're done, we'll add 2 to the stack pointer to deallocate int variable since we're done using it.

## Slide 9: Lab#4 Intro
  Lab#4 Assignment: Mixing C and Assembly
  Etch-a-sketch/paint program on the LCD display

## Slide 10: Todd’s old GCC example

## Slide 11: Mapping C to Assembly (gcc compiler)
C Version:
#include <msp430g2553.h>
int recursiveSummation(int numberToSum);
void main(void)
{
int my_number = 10;
my_number = recursiveSummation(my_number);
}
int recursiveSummation(int numberToSum)
{
if (numberToSum <= 0)
return 0;
else
return numberToSum + recursiveSummation(numberToSum - 1);
}
Generated Assembly Code:
main:
mov r1, r4
add #2, r4
sub #2, r1
mov #10, -4(r4)
mov -4(r4), r15
call #recursiveSummation
mov r15, -4(r4)
add #2, r1
recursiveSummation:
push r4
mov r1, r4
add #2, r4
sub #2, r1
mov r15, -4(r4)
cmp #1, -4(r4)
jge .L3
mov #0, r15
jmp .L4
.L3:
mov -4(r4), r15
sub #1, r15
call #recursiveSummation
add -4(r4), r15
.L4:
add #2, r1
pop r4
ret
Notes: Let's examine what's going on here.
The first line of code moves r1 (the stack pointer) into r4. The compiler is using r4 as the frame pointer. When you call a function (main() in this case), all of its local variables are allocated on the stack. We call the space on the stack used by a function a stack frame. However, the stack pointer changes as you allocate more variables on the stack. So a variable that was at 4(r1) at one point in your function could later be at 8(r1) if the stack pointer changes. The frame pointer ensures a consistent address for the same variable throughout the function. If we store the address of the base of the stack frame in the frame pointer, each variable will always be stored at the same place relative to the frame pointer - so a variable at 4(r4) will always be accessible at 4(r4).
So the first line of code is setting the frame pointer. Next, the compiler adds 2 to the frame pointer. In most functions, the first thing you do is push the frame pointer onto the stack via push r4 - main is the exception. Adding two puts the base of the stack frame below this value, which is what we want.
Next, the compiler subtracts two from the stack pointer. This is because we're allocating our int variable on the stack, so we're giving it two bytes. If we allocated two ints, the compiler would subtract 4 from the stack pointer.
Our first four instructions are identical to our first sample program. We're setting up the frame pointer and allocating our variable on the stack.
Next, we're moving our variable into r15. Remember, our ABI says that the first parameter to a function should be passed in through r15 - so we move our there.
Next, we call the recursiveSummation subroutine the compiler has created.
Once inside the recursiveSummation subroutine, we push the framePointer onto the stack so we don't destroy it. Then, we establish a new frame pointer and allocate a variable on the stack - just like we did in main.
Next, the compiler moves the parameter we passed in r15 into the variable we established. It compares the variable to 1.
If it's greater than or equal to 1, we jump to .L3 - the label that holds the code in our else case. We move our parameter into r15 (the register that holds the first parameter we pass to functions), subtract one, and call our recursiveSummation subroutine again. This code is the recursiveSummation(numberToSum - 1) piece of our code. The final instruction adds the current parameter to the result passed back in r15. This code is the return numberToSum + piece of our code.
If it's less than 1, we're finished. We move 0 into r15, deallocate our variable from the stack, retrieve the frame pointer we pushed initially, and return.
If you're interested in learning more, check out this Wikipedia reading on the Call Stack.
After we're done, we'll add 2 to the stack pointer to deallocate int variable since we're done using it.