## Slide 1: ECE 382 Lesson 13
Lesson Outline
  Peripherals
  Memory-Mapped IO
  Ports
  GPIO
  Multiplexing
Admin
  Lab 2 BitBucket report due COB Today (no penalty if turned in by Midnight Sunday)
  - Commit Message “Lab 2 notebook is ready to grade”
  BadLec5.asm Extra Credit Due Next Lesson

## Slide 2: Common Mistakes on Lab 1
Use of multiple .asm files (all functionalities should be in final .asm)
Lack detail on flowgraph (i.e. values and data outputs)
Didn’t include documentation in code header or didn’t have a header
Didn’t show Proof of Functionality (i.e. “Show me the memory!”)
Used Magic numbers instead of constants
  Constants should be in all CAPs
Not using the Example repo (missing sections or details)
  https://github.com/jfalkinburg/ECE_382_Lab_Ex
  Don’t copy entire code into readme
Code built in RAM (i.e. the .data section)
Missing 2 Additional Test Cases, didn’t test them, or didn’t account for edge cases, or didn’t explain the results
Effective use of BitBucket (need at least 3 commits with detailed comments for code)
Didn’t show me the Multiply algorithm or document the source
Poor Conclusion (i.e. Telling me what you did and what you learned)

## Slide 3: What do I want to see on the Lab 2 Notebook?
Use one .asm file for all functionalities and commit often
  Each Functionality should have a commit
  Effective use of BitBucket should be at least 3 commits with detailed comments
  Don’t forget code headers and comments and update subroutine headers
Show Proof of Functionality (i.e. “Show me the memory!”)
  Don’t include an image without explaining what it is and how it is important
  For A-Funct you should also tell me what the key in addition to the message
Update your flowgraph! Show me what registers you used to pass data
  If you did A or B-Funct you need to show me how you did it (i.e. Flowgraph)
Discuss any issues had in the debugging section
Conclusion – Paragraph that restates the purpose, discusses whether you achieved that goal, and tell me what you learned and how you can use this in the future.

## Slide 4: Peripherals
What are Peripherals?
MSP430G2xx Peripherals?
  MSP430 wikipedia:
  Watchdog Timer
  Universal Serial Communication Interface (USCI)
    Implements SPI and I2C protocols
    We'll use SPI to interface with the LCD in your black box
  Pulse Width Modulation (PWM)
    We'll use this later to drive the robot
  Temperature Sensor
  Multipliers
  Capacitive Touch I/O
    For working with touch screens, etc

## Slide 5: Ports
What are Ports? Examples?
Your LaunchPad Board has…
  Port 1, Pin 0 to Pin 7
  Port 2, Pin 0 to Pin 5 (where are pin 6 and 7?)

## Slide 6: 68HC12

## Slide 7: Multiplexing
Only 20 Pins !!! But want access to many more signals
  Therefore, each pin shares several signals  multiplexing
Use PxSEL1 and PxSEL2 to select signal for each pin
  The details are in the MSP430G2x53 2x13 Mixed Signal MCU Datasheet.

## Slide 8: Pitfall !!!
Let's say I wanted to make the UCA0SOMI function available on P1.1:
  ; 'from USCI' means this bit is set automatically by the USCI when enabled
  bis.b #BIT1, P1SEL
  bis.b #BIT1, P1SEL2

## Slide 9: How do we talk to Ports? Do I/O?
Two classic methods
  Memory-Mapped I/O (Motorola)
  Port-Mapped I/O [or Isolated IO] (Intel)
Memory-Mapped I/O
  I/O and memory SHARE the same address space
  Advantage
    Fewer instructions
    Can use all addressing modes
  Disadvantage
    Lose memory to IO
    Programmer mistakes
  How to use
    Mov #0x55, &P1OUT
    Mov #0x55, &0x0021
  User’s Guide p 333, Table 8-2 (BB pp 41)
  Watchdog Timer, page 341 (BB pp 42)

## Slide 10: How do we talk to Ports? Do I/O?
Port-Mapped I/O (Intel)
  I/O and memory have their own separate address space
  Advantage
    Don't lose memory for IO.
    Protects coder from mistakes.
  Disadvantage
    Need More Instructions (like In/Out)
    More restrictive addressing modes
  How to use
    Out #0x55, &PORT1
  Does Port-Mapped cheat?

## Slide 11: General Purpose Input Output (GPIO)
The registers used to configure GPIO are PxDIR, PxREN, PxOUT, and PxIN
  PxDIR configures which pins are input and which pins are output
    1 corresponds to output, 0 to input
  PxREN controls pull up / pull down resistors to avoid floating inputs.
  Writing to PxOUT controls the output of each pin
  PxIN allows you to read the values on these pins
Let's write a program that controls the onboard LEDs with the onboard push button
bis.b #BIT0|BIT6, &P1DIR
bic.b #BIT3, &P1DIR
check_btn: bit.b #BIT3, &P1IN ;push button is LOW on push
jz set_lights
bic.b #BIT0|BIT6, &P1OUT
jmp check_btn
set_lights: bis.b #BIT0|BIT6, &P1OUT
jmp check_btn
Any problem with this code?
Family Users Guide p 328
Blue Book pp 38

## Slide 12: Example Program
Input was FLOATING! Low is ground, High is floating, so use a pull- _________?
bis.b #BIT0|BIT6, &P1DIR ; output pin direction
bic.b #BIT3, &P1DIR ; input pin direction
bis.b #BIT3, &P1REN ; enable pin 3’s resistor
bis.b #BIT3, &P1OUT ; make it a pull-up? (trick)
check_btn: bit.b #BIT3, &P1IN
jz set_lights
bic.b #BIT0|BIT6, &P1OUT
jmp check_btn
set_lights: bis.b #BIT0|BIT6, &P1OUT
jmp check_btn
Modify code to toggle the LEDs when button is pressed (i.e. one LED on and one off)

## Slide 13
Figure 1.23 Logic levels and noise margins
Why Pullup and Pulldown Resistors are needed
Voltage Levels and Noise Margins

## Slide 14: Pitfall !!!
Anything wrong with this?
  mov.b #0xff, P1DIR
What do these commands do?
  mov.b #0b00001111, &P1DIR
  bis.b #0b00001111, &P1OUT
  mov.b #0xff, &P1OUT
  mov.b &P1IN, r5

## Slide 15: Inclass Exercise
Modify this program so the two LEDs always have the opposite value
bis.b #BIT0|BIT6, &P1DIR ; output pin direction
bic.b #BIT3, &P1DIR ; input pin direction
bis.b #BIT3, &P1REN ; enable pin 3’s resistor
bis.b #BIT3, &P1OUT ; make it a pull-up? (trick)
check_btn: bit.b #BIT3, &P1IN
jz set_lights
bic.b #BIT0|BIT6, &P1OUT
jmp check_btn
set_lights: bis.b #BIT0|BIT6, &P1OUT
jmp check_btn